## Slide 1
Notes across all examples
The following examples show simplified ‘ideal’ metering arrangements. This may not be needed or possible in all scenarios. Cumulative/actual metering as well as Difference metering solutions are within scope.
Values stated are annual MWh consumption figures recorded at the specific meter and so may not reflect actual load-flow in real time. Positive values represent demand consumption whilst negative values represent generation/export.
Any Generation TNUoS liability for each example is separately calculated and applied (i.e. additional to any Demand TNUoS liability)
Points X, Y and Z are all measured at the boundary point and reflect different ways of measuring flow/consumption at the boundary point. This assumes that the metering at the Boundary Point can separately report values X and Z;
  X = Gross Consumption: total demand consumption at the site (i.e. Final and Non-Final Demand)
  Y = Gross Final Demand Consumption: total Final Demand demand consumption at the site (i.e. removing any non-final demand).
  Z = Net Demand: Observed position when both Gross Consumption and Export volumes are summated.
Treatment of consumption measured at meter points A to D will not be affected by how that consumption is met (i.e. from onsite generation or supplied from the wider network)

## Slide 2
Transmission Network
Example 1 - Gross Consumption vs Gross Final Consumption vs Net Consumption
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
Meter A = +35 MWh
Meter C = +20 MWh
Meter E = -50MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
Final Consumption
Non-Final Consumption
Meter B = +35 MWh
Meter D = +10 MWh
Boundary Point
X, Y or Z
Observed at boundary point;
X = Gross Consumption = +100 (A+B+C+D) = Band 2
Y = Gross Final Consumption = +90 = Band 1. This can be calculated as A+B+C or X-D
Z = Net Consumption = +50 (A+B+C+D+E) = Band 1

## Slide 3
Transmission Network
Example 2 - generator with a small amount of Consumption.
(Omniscient view)
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Meter A = +35 MWh
Meter C = +20 MWh
Meter E = -500 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
Final Consumption
Non-Final Consumption
Meter B = +35 MWh
Y = +90 MWh
Z = -400 MWh
Meter D = +10 MWh

## Slide 4
Transmission Network
Example 2a - generator with a small amount of Consumption.
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Meter A = +35 MWh
Meter C = +20 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
If no additional metering installed, then Gross Consumption (X) used and allocated to band 2
If additional metering is installed & declaration provided, then Gross Final Consumption (Y) is used and allocated to band 1. This can be calculated as A+B+C. Declaration would also need to confirm method of calculating
Net metered position (Z) not used as boundary point separately reports value X
Final Consumption
Non-Final Consumption
Meter B = +35 MWh
Y = +90 MWh
Z = -400 MWh

## Slide 5
Transmission Network
Example 2b - generator with a small amount of Consumption
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
If no additional metering installed, then Gross Consumption (X) used and allocated to band 2
If additional metering is installed & declaration provided, then Gross Final Consumption (Y) is used and allocated to band 1. This can be calculated as X-D. Declaration would also need to confirm method of calculating
Net metered position (Z) not used as boundary point separately reports value X
Final Consumption
Non-Final Consumption
Meter D = +10 MWh
Y = +90 MWh
Z = -400 MWh

## Slide 6
Transmission Network
Example 3 - generator with equal ‘Consumption’
(Omniscient view)
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Meter A = +35 MWh
Meter C = +20 MWh
Meter E = -100 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
Final Consumption
Non-Final Consumption
Meter B = +35 MWh
Meter D = +10 MWh
Y = +90 MWh
Z = 0 MWh

## Slide 7
Transmission Network
Example 3a - generator with equal ‘Consumption’
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Meter A = +35 MWh
Meter C = +20 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
If no additional metering installed, then Gross Consumption (X) used and allocated to band 2
If additional metering is installed & declaration provided, then Gross Final Consumption (Y) is used and allocated to band 1. This can be calculated as A+B+C. Declaration would also need to confirm method of calculating
Net metered position (Z) not used as boundary point separately reports value X
Final Consumption
Non-Final Consumption
Meter B = +35 MWh
Y = +90 MWh
Z = 0 MWh

## Slide 8
Transmission Network
Example 3b - generator with equal ‘Consumption’
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
If no additional metering installed, then Gross Consumption (X) used and allocated to band 2
If additional metering is installed & declaration provided, then Gross Final Consumption (Y) is used and allocated to band 1. This can be calculated as X-D. Declaration would also need to confirm method of calculating
Net metered position (Z) not used as boundary point separately reports value X
Final Consumption
Non-Final Consumption
Meter D = +10 MWh
Y = +90 MWh
Z = 0 MWh

## Slide 9
Transmission Network
Example 4 - Consumption site with small onsite generation.
(Omniscient view)
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Meter A = +35 MWh
Meter C = +20 MWh
Meter E = -20 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
Final Consumption
Non-Final Consumption
Meter B = +35 MWh
Meter D = +10 MWh
Y = +90 MWh
Z = +80 MWh

## Slide 10
Transmission Network
Example 4a - Consumption site with small onsite generation.
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Meter A = +35 MWh
Meter C = +20 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
If no additional metering installed, then Gross Consumption (X) used and allocated to band 2
If additional metering is installed & declaration provided, then Gross Final Consumption (Y) is used and allocated to band 1. This can be calculated as A+B+C. Declaration would also need to confirm method of calculating
Net metered position (Z) not used as boundary point separately reports value X
Final Consumption
Non-Final Consumption
Meter B = +35 MWh
Y = +90 MWh
Z = +80 MWh

## Slide 11
Transmission Network
Example 4b - Consumption site with small onsite generation.
Single Site
Final Consumption
‘Mixed’ Consumption
Generator (Export)
X = +100 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
If no additional metering installed, then Gross Consumption (X) used and allocated to band 2
If additional metering is installed & declaration provided, then Gross Final Consumption (Y) is used and allocated to band 1. This can be calculated as X-D. Declaration would also need to confirm method of calculating
Net metered position (Z) not used as boundary point separately reports value X
Final Consumption
Non-Final Consumption
Meter D = +10 MWh
Y = +90 MWh
Z = +80 MWh

## Slide 12
Transmission Network
Example 5 - Consumption only site
(Omniscient view)
Single Site
Final Consumption
‘Mixed’ Consumption
X = +90 MWh
Meter A = +35 MWh
Meter C = +20 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
No generation/storage (and so no Non-Final Consumption), so Gross Consumption and Gross Final Consumption are the same.
Provision of a declaration would not affect the volumes used.
Final Consumption
Meter B = +35 MWh
Y = +90 MWh
Z = +90 MWh

## Slide 13
Transmission Network
Example 6 - Generator.
(Omniscient view)
Single Site
Generator (Export)
X = +10 MWh
Meter E = -200 MWh
Notes
Example Band Boundaries
Positive values are Import/Consumption
Negative values are Export/Generation
User Assets and/or Unlicensed Network
Band | Threshold
1 | <100 MWh
2 | =>100 MWh
With no declaration provided, it is assumed that the Gross Consumption is Final Consumption and so allocated to band 1 based on X.
With declaration, confirmed no Final Consumption at Site and so would not face Consumption residual charges as methodology isn’t applicable (i.e. allocated to a ‘zero charge’ band)
Non-Final Consumption
Meter D = +10 MWh
Y = 0 MWh
Z = -190 MWh

## Slide 14
 |  | Example 1 (Gross vs Net) | Example 2 (Gen w/ Dem) | Example 3 (Gen = Dem) | Example 4 (Dem w/ Gen) | Example 5 (Dem only) | Example 6 (Gen only)
Final Consumption | Meter A | +35 MWh | +35 MWh | +35 MWh | +35 MWh | +35 MWh | N/A
Final Consumption | Meter B | +35 MWh | +35 MWh | +35 MWh | +35 MWh | +35 MWh | N/A
Mixed Consumption | Meter C | +20 MWh | +20 MWh | +20 MWh | +20 MWh | +20 MWh | N/A
Non-Final Consumption | Meter D | +10 MWh | +10 MWh | +10 MWh | +10 MWh | N/A | +10 MWh
Export | Meter E | -50 MWh | -500 MWh | -100 MWh | -20 MWh | N/A | -200 MWh
No additional meters or declaration (Gross Consumption) | Volume X (A+B+C+D) | +100 MWh | +100 MWh | +100 MWh | +100 MWh | +90 MWh | +10 MWh
 | Band | 2 | 2 | 2 | 2 | 1 | 1
Additional meters & declaration (Gross Final Consumption) | Volume Y (A+B+C) or (X-D) | +90 MWh | +90 MWh | +90 MWh | +90 MWh | +90 MWh | N/A
 | Band | 1 | 1 | 1 | 1 | 1 | N/A
Net Consumption (for completeness) | Volume (A+B+C+D+E) | +50 MWh | -450 MWh | 0 MWh | +80 MWh | +90 MWh | -190 MWh
 | Band | 1 | 1 | 1 | 1 | 1 | N/A