## Slide 1: Charging For Active Network Management / Flexible Connections
Webinar - 15 May 2019
The Webinar will begin Shortly

## Slide 2: Webinar Aims
  To provide you with:
    - an update on our work
    - an explanation of our proposals
    - opportunity to ask questions/challenge
    - an overview of next steps

## Slide 3: Background
  Ofgem asked DNOs to jointly review the principles for connection charging for Active Network Management (ANM) schemes.
  The existing Common Connection Charging Methodology (CCCM) was developed against a backdrop of traditional engineering assets.
  The CCCM includes rules for the apportionment of asset reinforcement costs (where shared assets are swapped-out for larger ones)
  In contrast ANM/flexible connections avoid the need for reinforcement by sharing available headroom and utilising existing assets closer to their maximum operating parameters.
  ANM/flexible connections use advanced smart grid technology with their own costs.

## Slide 4: Developing Common Charging Principles
  “… compliance with the methodology results in charges which reflect, as far as is reasonably practicable (taking account of implementation costs), the costs incurred by the licensee in its Distribution Business”
  What are the costs?
  Capital costs of connection
  Enduring running costs
  How should costs be allocated?
  Recognition of wider benefits
  Different treatment of capital costs associated with different scheme types?
  Different treatment of enduring O&M costs to those applied to existing ‘standard’ connections?

## Slide 5: Recognising ‘flexible’ can be Minimum Scheme
  “The Minimum Scheme is the Scheme with the lowest overall capital cost (as estimated by us), solely to provide the Required Capacity.”
  Customers now have choices to request and accept less than 24/7 capacity continuity via a flexible connection
  Required Capacity can therefore both be defined both in MW and the extent to which customers are prepared to be flexible.
  Customer can still choose 24/7 continuity and in such circumstances the Minimum Scheme will not be a flexible connection and will include reinforcement.

## Slide 6: Defining types
  The following categorisation of ANM is proposed:
  Type 1 – Dedicated ANM: A flexible connection/ANM scheme managing constraint(s) where there are no customers downstream of the constraint(s) who could connect new or additional generation without being controlled by the ANM scheme
  Type 2 – Wide Area ANM: An ANM scheme managing constraint(s) where there are customers downstream of the constraint(s) who could connect new or additional generation without being controlled by the ANM scheme
  The key difference is that the Type 1 scheme only benefits specific participants (no wider benefits) whilst Type 2 enables other diverse users to operate un-curtailed (providing wider benefits)

## Slide 7: Single Customer without ANM

## Slide 8: Type 1: Dedicated Single Customer ANM

## Slide 9: Type 1: Dedicated Multiple Customer ANM

## Slide 10: Type 2: Wide Area ANM (Simple)

## Slide 11: Type 2: Wide Area ANM (Complex)

## Slide 12: ANM Charging – Proposed Cost Recovery
Cost Components | Type 1 Single | Type 1 Multiple | Type 2 Wide Area
Capital |  |  | 
Customer extension assets | Charged individually | Charged individually | Charged individually
End user control unit | Charged individually | Charged individually | Charged individually
Local system management unit | Charged individually | Shared between participants | Recovered via DUoS
Scheme management unit | Charged individually | Shared between participants | Recovered via DUoS
Central Management unit | N/A | N/A | Recovered via DUoS
Enduring O&M |  |  | 
Communications, licensing, other | Recovered via DUoS | Recovered via DUoS | Recovered via DUoS

## Slide 13: Next Steps
  Take on board feedback from today
  Conclude drafting of proposed changes to Common Connection Charging Methodology
  Present proposals to ENA Open Networks Steering Group – June 2019
  Submit DCUSA Change Proposal - June/July 2019