## Slide 1: GC0139
Data Exchange Options

## Slide 2: Cardinal Point Requirements of PC9 Data Submissions
Grid Code Submission | Demand/Generation Cardinal Point
Week 28 | GB NETS Peak
 | GSP Peak
Week 2 | GB NETS Minimum
 | Access Period GSP Summer Minimum GSP Summer Daylight Minimum
All ETI cardinal point in time data to be submitted with week 2 /28 submission. Only generation additions and removals need to be provided at the time of an ETI submission in the accompanying Appendix G. ETI submission will include a CIM model showing the revised structural data populated with Y0 demand data.
The following slides detail options for the combination of CIM format and excel schedule (or CIM table) submissions that deliver the above requirements in week 28 and week 2. For illustrative purposes these slides assume a typical DNO Licence area to have 20 GSPs that each have 6 connected BSPs.

## Slide 3: Option 1 – Minimum number of CIM files, augmented with BSP Schedules to reflect all the forecast scenarios
Week 28 GB NETS Peak Submission
1 CIM file
Submission
BSP Outturn
Representation
120 Data Tables
Submission
Detailing BSP Outturn
and 8 year forecast
(at GB NETS Peak)
Week 28 GSP Peak Submission
No CIM file
submission
120 Data Tables
Submission
Detailing BSP Outturn
and 8 year forecast
(at GSP Peak)
Week 28 (Summary)
1 CIM file
240 data tables
Note: It may be possible to present the data in the 240 (excel) data tables via a Steady State Hypothesis (SSH) file, but this would require extra DNO resource to convert the excel data files in to a SSH format.

## Slide 4: Option 1 - Continued
Week 2 GB NETS Minimum Submission
1 CIM file
Submission
BSP Outturn
Representation
120 Data Tables
Submission
Detailing BSP Outturn
and 8 year forecast
(at NETS Minimum)
Week 2 Access Period Submission
No CIM file
submission
120 Data Tables
Submission
Detailing BSP Outturn
(at GSP Access Period Peak)
and 8 year forecast

## Slide 5: Option 1 - Continued
Week 2 GSP Summer Minimum Submission
120 Data Tables
Submission
Detailing BSP Outturn
and 8 year forecast
(at GSP Summer Minimum)
Week 2 GSP Summer Daylight Minimum Submission
No CIM file
submission
120 Data Tables
Submission
Detailing BSP Outturn and
8 year forecast (at GSP
Summer Daylight Minimum)
Week 2 (Summary)
1 CIM file
480 data tables
It may be possible to present the data in the 240 (excel) data tables via a Steady State Hypothesis (SSH) file, but this would require extra DNO resource to convert the excel data files in to a SSH format.
No CIM file
submission

## Slide 6: Option 2 – All Cardinal Point Scenarios in CIM files
6
Week 28 GB NETS Peak Submission
4 CIM files
Submission
BSP Outturn, Y1,
Y5 & Y10
Representation
No Data Tables
Submission
Week 28 GSP Peak Submission
4 CIM files
Submission for
each of 20 GSPs
(total = 80)
One CIM Model for each of year Yr0 (Outturn) and forecasts for Yr1, Yr5 & Yr10 for each Cardinal Point
No Data Tables
Submission
Week 28 (Summary)
84 CIM files
No data tables
Notes: CIM Model 1 would represent the point in time of GSP1 peak demand, with the other GSPs being populated with their demand at time of GSP1 peak. CIM Model 2 -20 would follow these principles.

## Slide 7: Option 2 - Continued
Week 2 GB NETS Minimum Submission
4 CIM file
Submission
BSP Outturn, Y1,
Y5 & Y10
Representation
No Data Tables
Submission
Week 2 Access Period Submission
No Data Tables
Submission
4 CIM files
Submission for each
of 10 Access Groups (total=40)
BSP Outturn, Y1,
Y5 & Y10
Representation
Notes: CIM Model 1 would represent the point in time of Access Group 1 peak demand, with the other Access Groups being populated with their demand at time of Access Group1 min. CIM Model 2 -10 would follow these principles.
10 models for each of Y1, Y5m Y10
Total 40 models

## Slide 8: Option 2 - Continued
Week 2 GSP Summer Minimum Submission
No Data Tables
Submission
Week 2 GSP Summer Daylight Minimum Submission
Week 2 (Summary)
204 CIM file
No data tables
No Data Tables
Submission
4 CIM file
Submission for each
of 20 GSPs (total=80)
BSP Outturn, Y1,
Y5 & Y10
Representation
4 CIM file
Submission for each
of 20 GSPs (total=80)
BSP Outturn, Y1,
Y5 & Y10
Representation

## Slide 9: Option 2
Option 2 – Summary.
Not considered viable due to the large number of CIM files that would need to be created and exchanged

## Slide 10: Option 3
Option 3 – the use of Steady State Hypothesis (SSH) files which may be used reduce the need to either i) present different demand scenario data in excel spreadsheets (Option 1) or ii) reduce the number of CIM files that need to be exchanged (Option 2)
Steady State Hypothesis (SSH) file many be used to help reduce the volume of CIM files that would need to be compiled in Option 2 (assuming that its viable). This would be similar to Option 1 or 4, but the data tables would be captured within the CIM model package via a SSH file.
This should make compiling and using the information in the data tables easier.
A SSH file approach could be used as an alternative to providing ‘paper based’ Schedule 11 files – but there would be up to 10 SSH files to replace each of the Schedule 11 table – one for each forecast year.
We probably need to decide whether this approach to providing forecast data would be an option for DNOs or a mandated requirement in the code. This might be appropriate once DNOs and Users are comfortable and experienced using CIM data exchanges if its possible to automate the process.

## Slide 11: Option 4 – Minimum number of CIM files Augmented with BSP Schedules
Week 28 GB NETS Peak Submission
1 CIM file
Submission
BSP Outturn
Representation
20 Data Tables
Submission
Detailing GSP Outturn
(at NETs Peak)
and 8 year forecast
Week 28 GSP Peak Submission
No CIM format
submission
20 Data Tables
Submission
Detailing GSP Peak Outturn
and 8 year forecast
Week 28 (Summary)
1 CIM Model
40 data tables
Note: ditto option 1 via SSH etc
Notes: The key point here is that the CIM is populated with BSP outturn data but the forecasts are at a GSP level (as the present arrangement – and would require NGESO to make some modelling assumptions in their analysis)
This Option is similar to the present arrangements ie GSP based forecasts but with the structural data provided down to BSP level.

## Slide 12: Option 4 - Continued
Week 2 GB NETS Minimum Submission
1 CIM format
Submission
BSP Outturn
Representation
20 Data Tables
Submission
Detailing GSP Outturn
(at NETS Minimum)
and 8 year forecast
Week 2 Access Period Submission
No CIM format
submission
20 Data Tables
Submission
Detailing GSP Outturn
(at GSP Access Period Peak)
and 8 year forecast

## Slide 13: Option 4 - Continued
Week 2 GSP Summer Minimum Submission
20 Data Tables
Submission
Detailing GSP Outturn
(at GSP Summer Minimum)
and 8 year forecast
Week 2 GSP Summer Daylight Minimum Submission
No CIM format
submission
20 Data Tables
Submission
Detailing GSP Outturn
(at GSP Summer Daylight Minimum)
and 8 year forecast
Week 2 (Summary)
1 CIM Model
80 data tables
Note: ditto option 1 via SSH etc
No CIM format
submission

## Slide 14: Summary – data exchange for week 2 / 28
Option | No. Cim Files | No. Data Tables
1 | 2 | 720
2 | 288 | 0
3 | SSH* | SSH*
4 | 2 | 120
* SSH – Staedy State Hypothesis could be applied to Options 1, 2 & 4

## Slide 15: Recommendations for GC0139 consideration
Option 4 – this is the emerging preferred option (subject to confirmation by NGET)
Implications of Option 4
  SOW - All ETI cardinal point in time data to be submitted with week 2 submission. Only generation additions and removals need to be provided at the time of an ETI submission.
  SQSS – (access group compliance)