## Slide 1: CMP320 Island MITS Radial Link Security Factor
Jennifer Geraghty for SSE Generation Ltd.
Additional Slides for Special CUSC Panel Meeting
13th August 2019

## Slide 2: Background (1)
Defect
If a MITS node exists on an Island (served by a single radial subsea circuit to the mainland), CUSC dictates that a 1.8 Security Factor is applied to the single radial subsea circuit, even though only a single circuit (1.0) security exists.
This means islands would be paying 80% higher TNUoS charges on the local circuit element of their connection, which may render these projects unviable.

## Slide 3: Background (2)
This defect is very defined and specific -> therefore the solution very clear:
the 1.8 security factor should not be applied to the local circuit element for RIW.
CMP320 will result in:
  more cost-reflective charging for RIW (in line with Ofgem’s requirement to be……)
  Better alignment with the EU Renewable Energy Directive (2998/28/EC) which calls for non-discriminatory implementation of national industry codes, particularly for generation in peripheral regions with low population density.

## Slide 4: CMP213 Workgroup already agreed defect and solution
CMP213 (Project TransmiT) Workgroup
Agreed with the defect
Agreed with the solution
Solution did not make it into the approved alternative : WACM 2

## Slide 5: TransmiT CMP213 - Defect and solution
Original Proposal form – Identified the defect :
“In addition, where a significant proportion of the spur has no redundancy, but is still deemed to be part of the wider network for charging purposes, the length of that portion of the circuit in the transport model would be adjusted to compensate by multiplying its actual length by 1/(Locational Security Factor).” [emphasis added]
Final Modification Report – Workgroup agreed defect and solution :
1.57 “There was agreement amongst Workgroup members that the global security factor should not be applied to portions of radial island transmission connections that have no redundancy in any potential alternatives where the MITS definition is unchanged (i.e. where radial island circuits are classed as MITS).” [emphasis added]
“4.122 The Proposer noted that this proposed change to the charging definition of the MITS node would only be required for the Original proposal, as those potential alternatives accounting for diversity would naturally limit the concerns raised in paragraph 4.116, and there would be no requirement to change the existing definition [of MITS] on this basis.” [emphasis added]
“6.29 However, it was noted that the requirement for this security factor of 1.0 would still be required for all three diversity alternatives, where the proposed change to the definition of MITS would not be made.” [emphasis added]

## Slide 6: Why Urgency (1)
This modification is required to be treated with urgency due to imminent CfD auction (the imminent issue) and the resulting significant economic impact on parties wishing to participate in the upcoming CFD auction if this modification hasn’t been approved
Certainty on TNUoS charging is vital for projects if they were to bid into the imminent CFD round

## Slide 7: Why Urgency (2)
The current 1.8 Security Factor will distort competition and make it less likely for RIW to bid in the upcoming CFD auction
This will result in:
  The island link itself becoming unviable
  Jeopardising island security of supply
  Reduction in renewable generation which could contribute to the 2030 targets

## Slide 8: Timeline
CFD Bidding Window: 9th – 15th August
CFD results announced 6th – 9th September
Contracts signed by 24th – 7th October

## Slide 9: CMP320 Island MITS Radial Link Security Factor
Jennifer Geraghty for SSE Generation Ltd.
CUSC Panel 26th July 2019

## Slide 10: Background (1)
Defect
The definition of MITS means that it is possible, in certain circumstances beyond the control of the User, that a MITS node may be created on an Island (served by a single radial subsea circuit to the mainland). This results in the single circuit being classified as part of the ‘wider’ system for which a Security Factor of 1.8 is applied; even though only a single circuit (1.0) situation actually arises. This would result in non-cost reflective charges being applied to Generation based on the relevant Island.
Notes: MITS Node: A node with either (i) more than 4 Transmission Circuits; or (ii) 2 or more Transmission Circuits and a Grid Supply Point.
Radial circuits are single ‘spurs’ that link generation and/or demand in one location to the wider interconnected transmission network.

## Slide 11: Background (2)
What
The application of the Security Factor where a MITS node is located on an island which, in turn, is connected to the mainland on a single radial subsea circuit needs to be changed from 1.8 to 1.0, if the relevant circumstances apply
Why
This change is required to ensure that the charges paid by Generators located on Islands served by a single radial circuit pay more cost reflective charges.

## Slide 12: Background (3)
How
Amend Section 14 of the CUSC to apply a Security Factor of 1.0 (rather than 1.8) where a MITS node is located on an island which, in turn, is connected to the mainland on a single radial subsea circuit.

## Slide 13: Why Change (1)
Level of Redundancy is important
  Security factor for onshore local circuit is 1 or 1.8
  Security factor for wider (MITS) circuits is set at 1.8 (ie. it assumes inherent redundancy)

## Slide 14: Why Change (2)
Security factor has a direct impact on the local circuit tariff
This Results in a the cost of a MITS substation being inflated by 80% compared to a single (non-redundant) substation which is not cost-reflective of the actual redundancy

## Slide 15: Solution (1)
Amend Section 14 of the CUSC to apply a Security Factor of 1.0 (rather than 1.8) where a MITS node is located on an island which, in turn, is connected to the mainland on a single radial circuit.

## Slide 16: Justification against Relevant Objective (a)
That compliance with the use of system charging methodology facilitates effective competition in the generation and supply of electricity and (so far as is consistent therewith) facilitates competition in the sale, distribution and purchase of electricity;
Positive

## Slide 17: Justification against Relevant Objective (b)
That compliance with the use of system charging methodology results in charges which reflect, as far as is reasonably practicable, the costs (excluding any payments between transmission licensees which are made under and accordance with the STC) incurred by transmission licensees in their transmission businesses and which are compatible with standard licence condition C26 requirements of a connect and manage connection);
Positive

## Slide 18: Justification against Relevant Objective (c)
That, so far as is consistent with sub-paragraphs (a) and (b), the use of system charging methodology, as far as is reasonably practicable, properly takes account of the developments in transmission licensees’ transmission businesses;
Positive

## Slide 19: Justification against Relevant Objectives (d) & (e)
Compliance with the Electricity Regulation and any relevant legally binding decision of the European Commission and/or the Agency. These are defined within the National Grid Electricity Transmission plc Licence under Standard Condition C10, paragraph 1
Neutral
Promoting efficiency in the implementation and administration of the CUSC arrangements
Neutral
Better UK Compliance with the EU Renewable Energy Directive (2009/28/EC)
Positive

## Slide 20: Justification against Relevant Objectives
This Modification will ensure that TNUoS charges for Islands which have a MITS node; but are connected to the mainland transmission system via a single radial circuit; are more cost reflective than under the current CUSC baseline. This will better facilitate Relevant Objective (b).
In turn, by having more cost reflective charges, competition between generators will be enhanced, thus better facilitating Relevant Objective (a). Finally, this change will bring the baseline CUSC up to date as the transmission system evolves with the introduction of single radial spurs and MITs nodes to Island situation, which will better facilitate Applicable Objective (c).

## Slide 21: Governance
Given materiality we believe that self-governance or fast track governance arrangements are not appropriate in this case.
We believe that as with other recent CUSC Modifications (such as CMP305 and CMP294) that this proposal goes to Code Administrator Consultation.