## Slide 1: WHOLE ENERGY SYSTEM NETWORK PLANNING

## Slide 2
Prepared by: Angeliki Gkogka, Senior Consultant – Energy Strategy Advisory Maria Tolokonskaya – Consultant, Energy Strategy Advisory |  | Verified by: Sarah Kimpton– Vice President, Energy Transition |  | Approved by: Rafiek Versmissen – Head of Energy Strategy Advisory
Copyright © DNV 2023. All rights reserved. Unless otherwise agreed in writing: (i) This publication or parts thereof may not be copied, reproduced or transmitted in any form, or by any means, whether digitally or otherwise; (ii) The content of this publication shall be kept confidential by the customer; (iii) No third party may rely on its contents; and (iv) DNV undertakes no duty of care toward any third party. Reference to part of this publication which may lead to misinterpretation is prohibited.
Project name: | Project WHOLE ENERGY SYSTEM NETWORK PLANNING | DNV - Energy Systems DNV Services UK Ltd 30 Stamford St., London, SE1 9LQ
Report title: | Final report | 
Customer: | National Grid ESO | 
Customer contact: | Robert Gibson | 
Date of issue: | 11/08/2023 | 
Project No.: | 10435540 | 
Organisation unit: | Energy Strategy Advisory | 
Report No.: | 1 | 
Applicable contract(s) governing the provision of this report: |  | 
 | Innovation project funded through the Network Innovation Allowance (NIA) | 
Keywords: Whole Energy System, FSO
Objective: Understand the use cases for undertaking whole energy network planning across multiple energy vectors, as well as options available to National Grid ESO in the context of delivering the energy system transition.
This project has been completed prior to the introduction of the Strategic Spatial Energy Plan and the Regional Energy Strategic Planner role; any changes resulted from these developments will be addressed in future work.

## Slide 3: Table of contents
Chapter | Table of Contents | Slide
 | Executive summary……………………………………………………………………..…………………………. | 4 - 5
1 | Introduction……………………………………………………………………..………………............................ | 6 – 9
2 | Approach ……………………………………………………………………………………………………………. Scope and assumptions Phase 1 Phase 2 Phase 3 | 10 - 13
3 | Use cases………………………………………………………………............................................................. Methodology Detailed description | 14 - 34
4 | Principles…...………………………………………………………………………………………………………... Methodology Detailed description Illustrative Approach | 35 - 51
5 | Gap analysis and recommendations……………………………………………………………………………… Technologies Skills, knowledge, resources Co-ordination Business processes Policy | 52 – 59
6 | Next Steps…………………………………………………………………………………………………………… | 60 - 61
7 | Appendix……………………………………………………………………………………………………………... List of abbreviations | 62 - 63

## Slide 4
The use cases illustrate the complexity of the task for the FSO, which requires an understanding of both existing and potential future interactions between gas (natural gas and/or hydrogen) and electricity network infrastructure delivery and operations. With this understanding and through ongoing developments, the FSO must identify interdependencies, trade-offs and synergies to make recommendations as to the best outcome for “GB plc”. The challenge is that no use case is the same, and the “best” outcome is determined through interpretation of multiple interdependent and dynamic factors.
As a basis for the FSO’s approach to undertaking whole energy system planning, Project WESNP has articulated a set of principles to be followed by FSO in delivering its objectives, as well as a further set of criteria to be observed in fulfilling its duties:
Project WESNP has not otherwise sought to develop a detailed quantitative or qualitative options assessment methodology for the FSO.
Great Britain (GB) is an early mover towards whole energy system planning and the first developed energy industry to introduce the role of a Future System Operator (FSO). Joint planning for gas (natural gas and/or hydrogen) and electricity network infrastructure will not be a simple process and will require careful consideration, engagement and coordination across energy industry stakeholders. As part of Network Innovation Allowance1, Whole Energy System Network Planning (WESNP) Project seeks to enhance the understanding of whole energy network planning by the FSO, identifying use cases and establishing principles that the FSO could apply.
Project WESNP developed seven use cases which explored opportunities for co-optimisation of gas and electricity infrastructure that are relevant today, or that we expect to be relevant in the future. Inevitably, some use cases depended on the outcome of future market developments or policy decisions, which would ultimately impact other market, regulatory and technology developments. The use cases are not exhaustive, but represent a reasonable range of situations that the FSO can be expected to encounter in undertaking whole energy network planning. The use cases are:
Wind farm and electrolysis build
Wind farm and CCGT conversion to hydrogen
Industrial cluster and blue hydrogen hub
Hydrogen storage to maximise recovery or renewable energy
Optimising a nuclear plant connection
Transition of natural gas networks to low/zero carbon fuel networks
Flexibility of whole system options for long-term planning and stability
1] https://smarter.energynetworks.org/projects/nia2_ngeso038/
WESNP
Executive Summary

## Slide 5: Key Messages
Whole energy system planning is a complex process that involves collaboration between multiple stakeholders and requires the FSO to appraise multi-vector energy options and their respective trade-offs to recommend the optimal network infrastructure solution.
To enable whole energy system planning, the ESO and collective stakeholders will have to continue bridging the gap in knowledge and develop new cross-vector capabilities in data, processes, resources, and tools.
As a priority, the next steps for the FSO are to:
Continue coordinating with National Gas Transmission (NGT) to establish the basis for future collaboration, systems and data sharing, and skills development;
Co-ordinate closely with Ofgem and DESNZ to drive/support policy decisions that will ensure effective implementation and operation of the FSO;
Continue engaging closely with other stakeholders (e.g., TOs; DNOs; GDNs) to establish the basis for future collaboration as well as systems and data sharing, including alignment with previous work on the Centralised Strategic Network Planning (CSNP) process;
Develop new (and/or improved) data building, gathering and exchange processes and protocols, as well as develop IT-based solutions to be in place in time to support the FSO role;
Develop a detailed whole energy system planning processes to enable the unbiased and effective options assessment and network planning process; and
Develop the tools and processes needed for its options assessment process.

## Slide 6: Section 1: Introduction

## Slide 7: Introduction
Objective
The objective of Project WESNP is threefold:
  Understand use cases for undertaking whole energy system planning across multiple energy vectors (e.g. electricity, gas, hydrogen and CCUS);
  Establish principles for whole energy system planning; and
  Support the development of the whole energy system planning process and the evolution of the ESO into FSO.
  The FSO Role
In the April 2022 consultation, Ofgem and the government have set out their views on the objectives, duties and role of the FSO. It is proposed that the new body will keep all the ESO’s existing responsibilities and expand to new ones.
Supporting UK to achieve net zero 2050 will be one of the key objectives for the FSO, which means it will have to adapt its fundamental internal processes, such as system planning, operation and coordination, to achieve this objective. This could potentially mean that the FSO can no longer be technology agnostic in its decision-making.
Another important change is the addition of the long-term planning function for the gas (natural gas and/or hydrogen) transmission network. This extended planning remit will help co-optimise across energy vectors and release whole system benefits.
Background
The UK has set out ambitious environmental targets of becoming net zero by 2050, with an interim goal of decarbonising the power sector by 2035. Reaching net zero will require a significant coordinated effort, of which system planning and network development will be a key part.
As part of the energy transition, the Government committed to creating an independent Future System Operator (FSO) with responsibilities in both the electricity and gas systems. This new central body will ensure efficient energy planning, enhance energy security, and promote innovation to do so while minimising the cost to consumers.
In addition to the Centralised Strategic Network Planning (CSNP) process, which currently covers holistic network planning for electricity transmission, the FSO will also have the responsibility to develop strategic plans for the gas network (natural gas and/or hydrogen). Ultimately, the FSO will integrate all those plans into a cross-vector planning process which will include other vectors (e.g. CCUS), if and when relevant.
Great Britain is an early mover towards ‘multi-vector planning’ and the first developed energy industry to introduce an FSO role. Developing whole energy system planning will not be a simple process and will require careful consideration, engagement and coordination across the energy industry and beyond to deliver the best outcome for GB plc.
National Grid ESO tasked DNV to explore whole energy system planning by identifying potential use cases across multiple energy vectors, developing principles for whole energy system planning, and identifying actions required to facilitate this new role for the FSO.

## Slide 8: Project Scope
In this study, we used the following definition of the Whole System Approach:
Interactions across electricity, gas and other emerging markets (such as hydrogen and CCUS), both onshore and offshore, and between transmission and distribution systems
Based on this definition of the whole energy system and the roles of responsibilities of the FSO, as set out in the consultation, the project undertook the following activities:
Research and analysis: Conducted desk-based research seeking international evidence as the basis for research into the best practice on whole energy system analysis and design – informing draft use cases and an initial set of principles for whole energy system planning.
Stakeholder Workshops: Engaged with a range of sector representatives to test and enhance use cases. Explored the synergies that can be obtained in the cross-sector management and delivery of energy projects, to enable the energy transition efficiently and economically.
Analysis and Reporting: Updated use cases, identified of trade-offs in the decision-making process and refined principles for the analysis. Included gap analysis in the current evidence base for optimisation across vectors and technologies and provided recommendations for ESO to close gaps going forward and position the FSO role for maximum impact and efficiency.
This project sought to build an understanding of whole energy network planning through research and analysis of existing best practice, tested through stakeholder engagement, to deliver an actionable set of use cases and principles for National Grid ESO to evolve into the FSO.

## Slide 9: Purpose of this document
This is the final report of the Whole Energy System Network Planning Review project which summarises potential use cases for network analysis and planning across multiple energy vectors, and establishes principles for whole energy system planning.
The report is structured as follows:
Section 2 provides a detailed approach of the steps that we followed in order to complete the project and the deliverables.
Section 3 describes the use cases that were developed during the project
Section 4 discusses guiding principles for whole energy system planning, alongside our approach in developing these principles.
Section 5 provides the results of the gap analysis and recommendations
Section 6 proposes next steps for the FSO and GB energy industry.

## Slide 10: Section 2: Approach

## Slide 11: 2.1 Scope and assumptions
Assumptions
The first step of the project was to identify the roles and objectives of the FSO to confirm the scope of the study. We reviewed Ofgem and DESNZ’s responses to the consultation which outlined the remit of the FSO and tested our understanding with the ESO.
Whole system coordination is a multifaceted challenge spanning across various areas, from network design and planning to real-time operation and market development. However, the scope of this project involves electricity and gas (natural gas and H2) network planning only, covering the following technologies:
Nuclear
Onshore electricity
Offshore electricity
Natural gas supply
Heating
Hydrogen production
Electricity generation
CCUS
Flexibility/Storage
H2
Natural gas networks
CCUS
Hydrogen networks
Although the definition of a whole system approach includes transmission-distribution coordination of both electricity and gas networks, this project concentrated its analysis on the transmission level.
Scope
The project followed three phases using a combination of desk-top research, workshops with industry experts, and engagement with a wide range of energy industry stakeholders.
Phase 1
Literature review of whole energy system coordination
Phase 2
Stakeholder engagement
Phase 3
Gap analysis and reporting
Fig 2.2 – Technologies considered in this project
Fig 2.1 – Project scope

## Slide 12: 2.2 Phase 1
Literature review
We reviewed over 20 literature sources across the four areas: 1) policy and regulation, 2) project-level examples, 3) academia, and 4) thought leadership to gather best practice and/or recent developments in whole energy system planning. This research formed a foundation for the use cases developed as part of this project by identifying areas of further improvement and gaps in analysis.
The key insights were drawn from a range of sources and studies, such as the Long Duration Energy Storage Study prepared by DESNZ, academic work carried out by Imperial College London, University of Birmingham and others, Energy Networks Association projects.
We also covered innovation projects carried out by electricity and gas distribution networks (H100 Fife – SGN1 and Net Zero South Wales – WWU & NGED2, in particular) which studied the resilience of the electricity, gas and water sectors as the UK transitions to net zero and the contribution of nuclear energy to the energy mix.
The majority of the literature focused on theoretical models and simulation, with a few innovation trials, such as Integrated Development of Low-carbon Energy Systems (IDLES)3 and Whole Energy System Accelerator (WESA)4.
Use cases and principles
Following the literature review, we held internal workshops with experts across electricity, natural gas and hydrogen to develop eight initial use cases, focusing on the potential whole energy system optimisation problems the FSO will have to consider in the future, given the technologies identified on the previous slide.
Each use case considered the interaction between at least two different energy vectors, the stakeholders involved, associated trade-offs and benefits, key barriers and dependencies.
From the use cases we identified the type of decisions the FSO would need to make regarding trade-offs between electricity and gas, optimisation of infrastructure delivery and operation, as well as proving the right signals to developers, infrastructure providers and market participants.
These informed our initial view of the principles of the whole energy system optimisation that the FSO should apply to maximise synergies across vectors and deliver the most efficient and economic outcome for GB.
Most synergies have been identified for hydrogen, in particular with respect to the location of hydrogen plants and production methods.
Increased requirement for flexibility was another common theme, with various technologies offering viable solutions, such as power-to-x technologies and storage. A few sources highlighted the need for long-duration storage, mainly delivered by hydrogen, to increase system resilience and reduce balancing costs [5],[6],[7].
Fig 2.3 – Literature review sources
1] https://www.h100fife.co.uk/; 2] https://www.regen.co.uk/project/net-zero-south-wales/; 3] https://www.imperial.ac.uk/energy-futures-lab/idles/research/; 4] https://es.catapult.org.uk/tools-and-labs/whole-energy-systems-accelerator/; 5] https://ieeexplore.ieee.org/document/9762239; 6] https://www.dnv.com/focus-areas/hydrogen/forecast-to-2050.html; 7] https://assets.publishing.service.gov.uk/government/uploads/system/uploads/attachment_data/file/1095997/benefits-long-duration-electricity-storage.pdf
Notes: https://ieeexplore.ieee.org/document/9762239 P&S
https://www.dnv.com/focus-areas/hydrogen/forecast-to-2050.html DNV
https://assets.publishing.service.gov.uk/government/uploads/system/uploads/attachment_data/file/1095997/benefits-long-duration-electricity-storage.pdf

## Slide 13: 2.2 Phase 2 and Phase 3
Phase 2 - Stakeholder engagement
Having created initial use cases and principles in Phase 1, we then tested them with a wide range of stakeholders from both the electricity and gas side of the industry. These “challenge and review sessions” provided valuable feedback to enhance our thoughts on use cases, fundamental principles, and implementation requirements for the FSO.
We ran a series of workshops, including bilateral sessions with the ESO; a workshop with National Gas, Ofgem and DESNZ; and a workshop with ENA members. During these sessions participants broadly agreed with our proposed materials and provided additional insights that helped us refine the use cases, add new principles, and identify next steps.
We also excluded a use case on regional planning to avoid interference with the ESO’s response to the (at the time of writing) ongoing consultation.
We intentionally did not develop a use case with other sectors, such as water and transport, to focus this study on the immediate areas of FSO’s influence, namely gas and electricity transmission. We do acknowledge the importance of these other sectors in the energy transition and provide recommendations for further research that will look beyond the energy sector.
Phase 3 - Finalising use cases and principles, gaps and recommendations
Following our stakeholder engagement sessions, we refined and finalised the use cases and principles to reflect feedback from stakeholders.
As a last step, we performed a gap analysis in evidence and analytical requirements in both the electricity and gas sectors which are required for whole energy system planning. The identified gaps can be grouped into six categories:
Technologies;
Skills, knowledge and resources;
Coordination;
Business processes, tools, data and ICT;
Policy; and
Governance.
The gap analysis informed our recommendations for further work to advance the collective thinking to underpin the future FSO role.

## Slide 14: Section 3: Use Cases

## Slide 15: 3.1 Use Cases - Methodology

## Slide 16: 3.1 Use Cases - Methodology
This section describes the methodology used to develop use cases.
Methodology
The project team ran several workshops to define and build use cases. Initial use cases were developed using the following inputs:
  Insights from the literature review
  DNV’s previous projects and expertise
  Examples from wider industry projects (past and ongoing)
DNV and the ESO then held multiple external sessions with Ofgem, DESNZ, National Gas and ENA members to test them and receive feedback. The outputs of these sessions were used to enhance, update and finalise the use cases.
Definition of a use case
The first step towards developing the use cases was to define the use cases as a concept and articulate their key requirements for this project.
This study adopted the following definition for a use case:
Use Cases Design Criteria
This project sought to identify a reasonable spectrum of use cases representing a range of situations that the FSO would be expected to encounter when it undertakes whole energy system planning. The use cases were therefore not meant to be exclusive.
In order to ensure that the use cases were fit for purpose DNV articulated 5 design criteria that informed the development of the use cases. These were:
Focus on network infrastructure: The situation should describe a network infrastructure project, such as connection of new generation or demand, new H2 production, or transmission or distribution network reinforcement.
Whole energy system scope: The situation should explore infrastructure options that involve at least two different energy vectors (e.g., electricity, natural gas and/or hydrogen and CCS).
Involves a (potential) trade-off between time, size, location, scale, net zero contribution of infrastructure solution(s).
Representative of realistic whole energy system planning challenges: The situation should describe network planning challenges that the FSO and GB energy industry are already facing, or are expected to face, on the pathway towards net zero 2050.
Unique: The approach in each use case should reasonably avoid duplication of the main question that it is seeking to address.
“A use case is a situation where the FSO has to consider network infrastructure options with interactions between different energy vectors, such as gas, electricity or hydrogen, and explore the potential trade-offs and synergies to optimize the outcome for GB.”

## Slide 17: 3.1 Use Cases - Methodology
ID | This is a unique ID number for each use case. ID numbers range from UC1 to UC7.
Name | This field reflects a representative name for each use case.
Goal | This field summarises what the use case aims to achieve through the different network infrastructure options. It provides the context for the desired outcome from each problem statement.
“Networked Energy” Elements | This field is described in detail in the next section.
Associated Synergies/ Benefits | This field describes the whole energy system benefits that are sought in the specific use case and the opportunities for synergies across whole energy vectors. More details included in the next section.
Key Barriers and Dependencies | This fields describes barriers to implementation of the solution and/or key considerations that should be taken into account during the decision making process. It also summarises dependencies on industry developments and on other sectors, including barriers to the ESO’s stakeholders as well.
Stakeholders | Any organisation outside the ESO which has a direct interest in the use case or is impacted by the decision.
Description | Detailed description of the use case
What does it mean for the FSO? | This field is specific to the ESO and the project and addresses what the role of the FSO would be in each use case. For example, what should the FSO do? Is this relevant to FSO’s advisory role? Does it have an impact on network planning? Does the FSO need to facilitate coordination with other stakeholders?
Each use case comprises of the following fields which are described below:
Table 3.1 – Use case elements

## Slide 18: 3.2 Use Cases – Detailed Description

## Slide 19: 3.2 Overview of use cases
  This section provides an overview of the use cases developed as part of this study.
  The aim of these use cases was to demonstrate potential optimisation challenges the FSO will encounter with whole energy system network planning. Use cases do not show an ‘end state’ of the energy system at a certain time but rather offer an articulation of plausible whole system interactions. When and how these interactions might precisely materialise depends on many factors, such as system needs, policy targets, security of supply, etc.
  In general, all use cases considered challenges that were relevant today, or that we expected to be relevant in the future. Inevitably, some use cases depended on the outcome of future market developments or policy decisions, which would ultimately impact other market, regulatory and technology developments. For example, the government policy decision on hydrogen for heat decision, expected in 2026, will have a significant steer on the future development of hydrogen networks and hydrogen production.
  Finally, the study aimed to have a balanced and unbiased representation of the natural gas, electricity and hydrogen sectors to reflect the new responsibilities of the FSO that will extend beyond its current remit for electricity. All use cases involved interaction at least between two energy vectors (electricity and natural gas, electricity and hydrogen, natural gas and hydrogen).
  We developed seven use cases, which are summarised in the diagram on the next slide. These are:
  Wind farm and electrolysis build
  Wind farm and CCGT conversion to hydrogen
  Industrial cluster and blue hydrogen hub
  Hydrogen storage to maximise recovery or renewable energy
  Optimising a nuclear plant connection
  Transition of natural gas networks to low/zero carbon fuel networks
  Flexibility of whole system options for long-term planning and stability
  Slides 22-35 provide a detailed description for each of these use cases.
  This list is not exhaustive, and we acknowledge there are other whole energy system uses cases, such as interaction with data centres and heat networks among others, but these were deemed outside of the scope of Project WESNP. The purpose of the use cases described in this project was to not to reflect a finite list, but rather to provide typical examples of network infrastructure planning challenges.
  Furthermore it is important to note that every use case refers to a single optimisation problem which required a single infrastructure solution. Naturally, this would change when considering the wider GB planning strategy, where a variety of options could be applicable subject to the specifics of the problem. For example, network reinforcement may be an optimal infrastructure solution in one instance, while at another location installing an electrolyser could optimise network planning.
  Figure 3.2 on the next slides provides a schematic overview of the use cases.

## Slide 20
3.2 Summary of use cases
INDUSTRIAL CLUSTER
H2 STORAGE
ELECTROLYSER
CCGT
ONSHORE WIND
OFFSHORE WIND
CCUS
1
2
3
4
NUCLEAR PLANT
ELECTROLYSER
5
Wind farm and electrolysis build
Wind farm and CCGT conversion
Industrial cluster and blue hydrogen hub
Hydrogen storage to maximise recovery of renewable energy and provide seasonal storage
Optimising a nuclear plant connection
HEAT
H2 CCGT
ELECTROLYSER
Convert from gas to hydrogen
POWER GENERATOR
H2 STORAGE
BLUE H2 PLANT
6
Transition of natural gas networks to low/zero carbon fuel networks
DHN
7
Flexibility of whole system options for long term planning and stability
ELECTROLYSER
OFFSHORE WIND
Constraint
ELECTRICITY TRANSMISSION
Constraint
H2 NETWORK
NAT.GAS NETWORK
Fig 3.2 – Summary of use cases
Electricity network
Gas network
Hydrogen network
Carbon network
Heat network

## Slide 21
INDUSTRIAL CLUSTER
H2 STORAGE
ELECTROLYSER
CCGT
ONSHORE WIND
CCUS
2
3
4
NUCLEAR PLANT
ELECTROLYSER
5
Wind farm and CCGT conversion
Industrial cluster and blue hydrogen hub
Hydrogen storage to maximise recovery of renewable energy and provide seasonal storage
Optimising a nuclear plant connection
HEAT
H2 CCGT
ELECTROLYSER
Convert from gas to hydrogen
POWER GENERATOR
H2 STORAGE
BLUE H2 PLANT
6
3.2 Use case 1
Future of gas network
DHN
7
Flexibility of whole system options for long term planning and stability
OFFSHORE WIND
Constraint
NAT.GAS NETWORK
OFFSHORE WIND
1
Wind farm and electrolysis build
ELECTROLYSER
Constraint
ELECTRICITY TRANSMISSION
H2 NETWORK
Electricity network
Gas network
Hydrogen network
Carbon network
Heat network

## Slide 22
UC1: WIND FARM AND ELECTROLYSIS BUILD |  |  | 
Goal | Maximise the amount of wind capacity built and maximise the energy recovery from that capacity. | Associated Synergies/ Benefits | Enable growth in distributed energy resources Accelerate H2 economy (accelerate net zero) Avoid curtailment of renewable power
“Networked Energy” Elements | Onshore and offshore electricity transmission; hydrogen production; flexibility and storage |  | 
Stakeholders | FSO; electricity transmission owners; gas/hydrogen network owners; wind farm owners; hydrogen producers; H2 electrolyser & storage owners/operators | Key Barriers and Dependencies | Speed-of-delivery – technology readiness levels Location: Geographical – H2 storage geology, water availability Demand proximity – Industrial / commercial / domestic System – E, G and H network proximities & capacities
Description | A new offshore wind farm requires an electricity transmission connection behind a constrained area of the electricity network. Depending upon the nature (timing, duration, degree) of the constraint, the appetite of the windfarm developer to adopt a single long-term customer, and the regional H2 development strategy, a direct connection to an electrolyser might be a viable alternative to a new or reinforced electricity transmission connection. With adequate H2 storage and transmission, the wind farm would then generate green H2 without being curtailed. The electrolyser could be located on land or offshore, depending upon the type and location of H2 consumption and associated transport facilities (particularly whether building new terrestrial/subsea pipeline or onshore/offshore tanker docking facilities). The alternative option would be to progress with reinforcing the electricity network to accommodate the additional capacity and potentially consider co-location with storage. Such co-optimised location of two energy vectors should boost (investability in) green H2 production, comprising a significant step towards net zero. The success of such an arrangement would depend entirely upon the type of connection agreement between the wind farm, the electrolyser and the grid. The US recently saw the largest PPA ever between a green H2 facility and a wind farm, indicating that there could be a cost-effective future for wind farms to supply the H2 market rather than (just) the electricity market. The optimisation for the FSO and GB energy industry will be to achieve the initial goal of this use case (i.e. maximise wind capacity and energy recovery), whilst juggling energy vectors to find the balance between net zero targets, Costs, Efficiency, Speed of delivery and potential environmental impact of the solution. For example, the FSO will need to consider whether instead of reinforcing the electricity network, there could be a strategically placed electrolyser that will produce green hydrogen during the periods of high wind and low electricity demand, and which might need supporting network infrastructure. This would reduce/eliminate the need to pay to curtail the windfarm. |  | 
What does it mean for the FSO? The role of FSO would be to: Manage the process by which customers connect to and make use of the electricity transmission system. Develop a planning process taking into consideration all the energy vectors to plan development of each energy system. This planning process will enable the FSO to determine the optimal solution to avoid curtailment of the wind farm. Design products to allow different vectors e.g., H2 to take part in different markets to maximize the use of renewable energy. The role of the FSO may also expand to include advice regarding: The hydrogen, gas and electricity strategies for the region. The potential for building a H2 storage, including its location and size. Hydrogen transportation methods either via a local H2 network, transmission H2 network or mobile transportation, such as ship. Furthermore, consideration will include storage capacity and location. | To be completed at later phase |  | 
H2

## Slide 23
INDUSTRIAL CLUSTER
ELECTROLYSER
CCUS
3
4
NUCLEAR PLANT
ELECTROLYSER
5
Industrial cluster and blue hydrogen hub
Hydrogen storage to maximise recovery of renewable energy and provide seasonal storage
Optimising a nuclear plant connection
HEAT
POWER GENERATOR
H2 STORAGE
BLUE H2 PLANT
6
3.2 Use case 2
Future of gas network
DHN
7
Flexibility of whole system options for long term planning and stability
OFFSHORE WIND
OFFSHORE WIND
1
Wind farm and electrolysis build
ELECTROLYSER
Constraint
H2 STORAGE
CCGT
ONSHORE WIND
2
Wind farm and CCGT conversion
H2 CCGT
ELECTROLYSER
Convert from gas to hydrogen
Constraint
NAT.GAS NETWORK
ELECTRICITY TRANSMISSION
H2 NETWORK
Electricity network
Gas network
Hydrogen network
Carbon network
Heat network

## Slide 24
UC2: WIND FARM AND CCGT CONVERSION TO HYDROGEN |  |  | 
Goal | Optimise the type and size of a new wind farm connection near an existing CCGT where there is potential to grow the local or regional H2 economy | Associated Synergies/ Benefits | Enable growth in distributed energy resources Energy cost savings Accelerate H2 economy (accelerate net zero) Maximise value of existing infrastructure/assets
“Networked Energy” Elements | Onshore and offshore electricity transmission - energy supply; gas transmission - energy demand; hydrogen production, storage & transmission - energy supply |  | 
Stakeholders | FSO; Electricity + Gas + H2 transmission companies; wind farm developer; CCGT own.er/operator; H2 electrolyser & storage owners/operators | Key Barriers and Dependencies | Capacity of current & future expected wind farm connections at this GSP Space and permissions (planning & environmental) to build electrolyser Geology and timescales (~ 10y) needed to provide H2 storage Space to expand GSP to suit new connections Political urgency to develop and serve the H2 economy from this node Cost-effectiveness, including of the H2 supply and CCGT conversion
Description | A developer applies for a new onshore/offshore wind farm connection at a GSP where a CCGT is in operation. The additional GSP export would expose a capacity constraint. It is known that the CCGT plant will come to closure by 2035. However, the wind farm connection application is for 2025. The wind farm connection options include: Depending upon the degree of constraint, reinforcing the grid to accommodate both CCGT and wind farm exports (avoids curtailment, maximizes renewable energy capture) Closing the CCGT 10 years early, and connecting the windfarm (avoids reinforcement, allows early capture of renewable energy) Avoiding both curtailment and network reinforcement by creating a local electricity demand in the form of electrolyser and H2 storage. Converting the CCGT to burn H2 would retain dispatchability and resilience, whilst feeding the H2 network would boost the H2 economy The choice of connection option here will require consideration of, amongst other things: Availability of an H2 network connection (or the proximity of other (present or future) H2 applications such as industry, space heating and transport) The local impact of UK’s energy transition plans, including factors such as local use of H2 / natural gas blending, temporary adoption of blue H2, and transition to H2 networks The required contribution to electricity system inertia / resilience, and whether the CCGT becomes a peaking plant. The speed at which CCGT conversion could take place and the H2 supply could be established – what indirect influence would the FSO have on this and on wind farm sizing? |  | 
What does it mean for the FSO? The role of FSO would be to: Collaborate with all energy vectors and coordinate strategies to optimise cost, security & resilience of GB's energy supplies in the transition to net zero Plan the energy transmission network to support this overall picture, optimising the Synergies identified above and considering the Barriers and Dependencies Advise Government on the GB energy strategy and on markets required to facilitate Within this plan, consider the local and national factors that this windfarm opportunity impacts, and select the optimum connection investment for this and all similar applications Prepare and justify appropriate electricity network plans, and enabling investments to speed the NZ transition and exploit new renewables connections in a timely manner Develop a strategy to facilitate enabling investment in key long-lead time energy assets (e.g., hydrogen storage, N-S electricity transmission) so that they facilitate the overall UK transition to NZ | To be completed at later phase |  | 
H2

## Slide 25
ELECTROLYSER
4
NUCLEAR PLANT
ELECTROLYSER
5
Hydrogen storage to maximise recovery of renewable energy and provide seasonal storage
Optimising a nuclear plant connection
HEAT
POWER GENERATOR
H2 STORAGE
6
3.2 Use case 3
Future of gas network
DHN
7
Flexibility of whole system options for long term planning and stability
OFFSHORE WIND
OFFSHORE WIND
1
Wind farm and electrolysis build
ELECTROLYSER
Constraint
H2 STORAGE
CCGT
ONSHORE WIND
2
Wind farm and CCGT conversion
H2 CCGT
ELECTROLYSER
Convert from gas to hydrogen
Constraint
H2 NETWORK
INDUSTRIAL CLUSTER
CCUS
3
Industrial cluster and blue hydrogen hub
BLUE H2 PLANT
NAT.GAS NETWORK
ELECTRICITY TRANSMISSION
Electricity network
Gas network
Hydrogen network
Carbon network
Heat network

## Slide 26
UC3: INDUSTRIAL CLUSTER AND BLUE HYDROGEN HUB |  |  | 
Goal | Optimise gas, hydrogen, CCS and electricity system operation including the role of storage | Associated Synergies/ Benefits | Stimulate local economy Accelerate H2 economy (accelerate net zero)
“Networked Energy” Elements | CCS; hydrogen production; natural gas supply; flexibility/ storage (Tx); onshore electricity and gas networks; |  | 
Stakeholders | Natural gas network, hydrogen production plant owner, CCS and hydrogen network owners and users, electricity transmission owner | Key Barriers and Dependencies | Interdependency between power grid capacity, natural gas and hydrogen pipelines, CCUS capacity and hydrogen power generation capacity Barriers include long lead times for geological hydrogen storage and the need to coordinate the above interdependencies
Description | A blue hydrogen production plant will be developed at an industrial cluster. The hydrogen plant will need connections to natural gas, carbon dioxide and hydrogen networks. The blue hydrogen production systems work most efficiently at a constant output, and this includes the CCS facilities. The low-carbon hydrogen will be used within the industrial cluster, which is almost certain to have a variable hydrogen demand over time. H2 storage facilities will be required to smooth H2 production. The low-carbon hydrogen could also be used by a hydrogen peaking plant, in which case connection to the electricity grid and a larger H2 storage facility will also be required. The optimisation for the FSO and key stakeholders would be to consider: Is the development of these technologies at scale the optimum way to meet net zero targets i.e. should industry invest now in transitional blue H2 or immediately support an enabling investment in green H2. For example, in the longer-term solution green hydrogen may be preferred to blue hydrogen which could be produced locally, offshore and/or delivered by the gas network. The impact of this hub on the whole energy system and how it fits into their strategy and network planning. The optimal use for low-carbon hydrogen. Should it be used only to supply the demand of the industrial cluster or could it be used by a hydrogen peaking plant to facilitate electricity system balance and resilience? |  | 
What does it mean for the FSO? Ultimately the FSO will need to: Assess the impact of these facilities on electricity network planning as well as on the long-term gas strategic planning. For example the FSO will need to be cognisant of: the operational requirements of the reforming and CCS plant the H2 peaking plant impact balancing the power system whether transmission or distribution connection is required the long-term growth of this cluster. (i.e. how much growth of the facility should the FSO cater for? Will the facilities be constrained in the future by the demands from green H2 production and electrification). Develop skills and capabilities to investigate the role of H2 storage for security of supply Assess the role of green and blue hydrogen in GB’s net zero strategy. | To be completed at later phase |  | 
H2
CCUS

## Slide 27
NUCLEAR PLANT
ELECTROLYSER
5
Optimising a nuclear plant connection
HEAT
6
3.2 Use case 4
Future of gas network
DHN
7
Flexibility of whole system options for long term planning and stability
OFFSHORE WIND
1
Wind farm and electrolysis build
ELECTROLYSER
Constraint
H2 STORAGE
CCGT
ONSHORE WIND
2
Wind farm and CCGT conversion
H2 CCGT
ELECTROLYSER
Convert from gas to hydrogen
Constraint
INDUSTRIAL CLUSTER
CCUS
3
Industrial cluster and blue hydrogen hub
BLUE H2 PLANT
NAT.GAS NETWORK
ELECTROLYSER
4
Hydrogen storage to maximise recovery of renewable energy and provide seasonal storage
POWER GENERATOR
H2 STORAGE
OFFSHORE WIND
H2 NETWORK
ELECTRICITY TRANSMISSION
Electricity network
Gas network
Hydrogen network
Carbon network
Heat network

## Slide 28
UC4: HYDROGEN STORAGE TO MAXIMISE RECOVERY OF RENEWABLE ENERGY |  |  | 
Goal | Optimise hydrogen storage design and plan to facilitate net zero, ensure security of supply and facilitate competitive markets. | Associated Synergies/ Benefits | Contribute to the Long Duration Storage Strategy Reduce emissions from electricity system balancing Facilitate innovation
“Networked Energy” Elements | Electricity generation, onshore electricity and gas networks, hydrogen production, flexibility/storage |  | 
Stakeholders | Renewable generators, storage operators, hydrogen networks, peaking plant, electricity networks, Crown Estate | Key Barriers and Dependencies | Interdependency between renewable electricity generation, power grid capacity, electrolysis capacity, hydrogen storage, hydrogen pipelines and hydrogen power generation capacity. Barriers include long lead times for geological hydrogen storage and the need to coordinate the above interdependencies Funding for the gas networks
Description | One of the UK Government’s ambition is to increase offshore wind capacity to 40 GW by 2030 as part of reaching the net zero target by 2050. Although this power capacity will generally facilitate net zero, security of supply and system balancing, the networks will also need to plan for long periods of low wind output and remaining electricity demand will need to be met by other sources. For example, when heating demand is very high and wind power generation is low for 2-3 days, long duration storage is required. Whilst natural gas peaking plant provides a solution to this issue, this does not align with net zero and the targets on the use of unabated gas. Hydrogen storage and peaking power generation could provide a viable solution (as set out in the recent BEIS’ Long Duration Energy Storage report and the Climate Change Committee’s decarbonised power system report), but several factors need to be considered by the FSO. The FSO can inform decision making on the following: 1. When is H2 storage required? The lead time for developing hydrogen storage is from 5 to 10 years. So operators need to start investing and planning for hydrogen storage well before hydrogen can be used. Delivery time is critical for net zero progress as well as to ensure security of supply and system balancing. 2. How much H2 and what are the suitable H2 storage forms for different conditions? The FSO could provide advice and optimise the hydrogen storage design including considerations such as the volume of storage required, the scale of storage required, withdrawal rate, energy losses of hydrogen as hydrogen is produced from power, stored and then fed back to the network. 3. Where should the H2 storage facilities be located? The location of H2 storage facilities is a difficult decisions as it depends on the location of the generation facility, the transportation options for H2 and the geological condition of the area (e.g. in case of salt cavern H2 storage). In addition, the FSO will need to consider the location of H2 storage with regard to the location of the electricity network constraints. 4. At later stage, the FSO will also need to consider how to operate a system with all the different flexible sources (e.g. hydrogen storage, vehicle to grid, batteries) and facilitate free and fair markets for the different technologies. |  | 
What does it mean for the FSO? The role of the FSO would be to: Contribute to strategic national decisions on hydrogen storage capacity. Provide advice to Government based on forecasts of required hydrogen power generation capacity to ensure the smooth running of a decarbonised power sector. Complement the advice provided by geological organisations through advising on where hydrogen storage would make sense from an above-ground perspective e.g. in relation to location of power and hydrogen transmission. | To be completed at later phase |  | 
H2

## Slide 29
6
3.2 Use case 5
Future of gas network
7
Flexibility of whole system options for long term planning and stability
OFFSHORE WIND
1
Wind farm and electrolysis build
ELECTROLYSER
Constraint
H2 STORAGE
CCGT
ONSHORE WIND
2
Wind farm and CCGT conversion
H2 CCGT
ELECTROLYSER
Convert from gas to hydrogen
Constraint
INDUSTRIAL CLUSTER
CCUS
3
Industrial cluster and blue hydrogen hub
BLUE H2 PLANT
NAT.GAS NETWORK
ELECTROLYSER
4
Hydrogen storage to maximise recovery of renewable energy and provide seasonal storage
POWER GENERATOR
H2 STORAGE
OFFSHORE WIND
NUCLEAR PLANT
ELECTROLYSER
5
Optimising a nuclear plant connection
HEAT
DHN
H2 NETWORK
ELECTRICITY TRANSMISSION
Electricity network
Gas network
Hydrogen network
Carbon network
Heat network

## Slide 30
UC5: OPTIMISING A NUCLEAR PLANT CONNECTION |  |  | 
Goal | Optimise a nuclear plant connection to enable system operation and balancing | Associated Synergies/ Benefits | Stimulate nuclear economy Facilitate innovation Decarbonisation of domestic Promote cross-sector co-ordination
“Networked Energy” Elements | Nuclear Power plant, flexibility/ Storage (Tx), H2 production, onshore electricity and gas networks, |  | 
Stakeholders | Nuclear plant owner, TO, H2 electrolyser & storage owners/operators, DH scheme owners/ operators. DNO, directly connected demand (e.g. Industrial site) | Key Barriers and Dependencies | Nuclear power plant locations are limited and they have a long lead time to be built and operational Technology-readiness of thermo-chemical electrolysis Benefits and feasibility of district heating are limited to a small number of large densely populated areas, which might not be located near a power plant Location of the plant - in case of electrolysis - should take into consideration hydrogen transport and storage facilities High upfront cost
Description | A nuclear power plant produces low-carbon electricity that could: directly supply electricity to the grid as primary use; produce electrical power to an electrolyser for hydrogen production – the attractiveness of nuclear power is that it is a firm energy source. Plant siting should be carefully chosen to optimise the costs for hydrogen infrastructure and hydrogen storage; produce heat and power for high-temperature thermo-chemical hydrogen production– hydrogen production using this process is very efficient; supply a District Heating scheme. The optimisation of the nuclear plant connection will require consideration of, amongst other things: The location of the nuclear plant and the hydrogen/electricity export to the network The size of the plant and its operation (e.g. combined hydrogen/ electricity production, combined heat/ electricity production) The availability of hydrogen and electricity networks The environmental and community impacts Other factors to be considered include that there is a limited range of nuclear licensed sites available and proximity to large quantities of cooling water will also be required. Where the nuclear plant provides power to standard electrolysers, there is an option to switch to exporting power to the electricity grid. The operational profile of the nuclear plant and its outputs would also have a significant impact on electricity system operation and balancing. For example, it may not be the optimal solution to build nuclear power to provide peak power to supplement variable renewable, but it may be more cost effective to build a relatively small capacity that is continuously producing hydrogen as a strategic reserve. |  | 
What does it mean for the FSO? The role of FSO would be to: Manage the process by which new electricity customers connect to and make use of the transmission system Engage and collaborate with other energy vectors and stakeholders – as mentioned above - to coordinate strategies to optimise cost, security & resilience of GB's energy supplies in the transition to NZ Advise government on how to optimise a combined/hydrogen electricity production, which would probably be less cost effective than hydrogen from renewable sources. Keep a balance between market – led decisions and other advantages related to system operation (e.g. connecting an electrolyser may help to avoid expensive starts/stops of the nuclear unit and keep it running up or above its minimum part load power). Advise government on the impact of different options on whole energy strategic network planning and system operation. Advise government on the timeline of delivering this “enabling investment” | To be completed at later phase |  | 
H2

## Slide 31
3.2 Use case 6
7
Flexibility of whole system options for long term planning and stability
OFFSHORE WIND
1
Wind farm and electrolysis build
ELECTROLYSER
Constraint
ONSHORE WIND
2
Wind farm and CCGT conversion
Constraint
CCUS
3
Industrial cluster and blue hydrogen hub
ELECTROLYSER
4
Hydrogen storage to maximise recovery of renewable energy and provide seasonal storage
POWER GENERATOR
H2 STORAGE
OFFSHORE WIND
NUCLEAR PLANT
5
Optimising a nuclear plant connection
HEAT
DHN
ELECTRICITY TRANSMISSION
6
Transition of natural gas networks to low/zero carbon fuel networks
H2 STORAGE
CCGT
H2 CCGT
ELECTROLYSER
Convert from gas to hydrogen
INDUSTRIAL CLUSTER
BLUE H2 PLANT
NAT.GAS NETWORK
ELECTROLYSER
H2 NETWORK
Electricity network
Gas network
Hydrogen network
Carbon network
Heat network

## Slide 32
UC6: TRANSITION OF NATURAL GAS NETWORKS TO LOW/ZERO CARBON FUEL NETWORKS |  |  | 
Goal | Running the electricity networks during partial switchover of gas networks to hydrogen. Efficient and co-ordinated network planning for gas (including biomethane) and hydrogen networks | Associated Synergies/ Benefits | Decarbonisation of domestic and industrial heat Support local economies Wider societal benefits
“Networked Energy” Elements | Onshore electricity and gas networks; hydrogen production; CCUS; onshore electricity generation; |  | 
Stakeholders | Natural gas producers and users, hydrogen producers and users, power generators, storage operators, biomethane producers, gas and hydrogen networks | Key Barriers and Dependencies | Interdependencies between gas network operation and power generation facilities, including CCGTs, OCGTs and gas engines that may be able to run on either hydrogen or methane. The main barrier is the uncertainty of the future role of gas networks – hydrogen, biomethane, natural gas or decommissioned.
Description | If the 2026 decision on the future of the gas networks allows some, or all, of the gas network to convert to hydrogen, the FSO will need to decide how it will operate the power network with an additional type of gas on the system. Pipelines, directly connected customers, gas distribution offtakers and CCGTs will be compatible with either natural gas or hydrogen. The capacity to supply GB with hydrogen will not develop overnight. The H2 networks strategy can take different directions. For example, we can convert zones of the system to 100% hydrogen, and we must consider the milestones to be in place to achieve this. There is also the option to blend natural gas with hydrogen in the NTS or electrify some zones and decommission some of the gas networks entirely. In parallel, GB’s biomethane production will grow and this can be injected directly into existing gas networks with minimal changes. In some more rural regions, it might be possible to run part of the gas network primarily on biomethane if there is some electrification of demand – in these areas it will make less sense to convert to hydrogen or decommission gas networks. The FSO’s role expands across a number of considerations: The FSO will need to consider the impact of all these changes on electricity system operation and system balancing whilst maintaining security of supply – including hydrogen produced from electrolysis and transported through gas networks to serve hydrogen peaking power plants. As part of FSO’s strategic network planning and advisory role the FSO could provide an objective opinion on the order, timing and development of future hydrogen conversion schemes, and biomethane expansion, whilst maintaining security of supply and taking into account locational constraints and opportunities. A desired outcome of this process would be a resilient and decarbonised energy system during the transition of the gas networks from natural gas to hydrogen and biomethane. |  | 
What does it mean for the FSO? The role of the FSO would be to: Ensure security of supply and effective system operation for the electricity system during the transition of gas networks, which will affect the supply of gases to some dispatchable power generation facilities. Facilitate co-ordination and collaboration with key stakeholders so that gas network developments are taken into account in strategic electricity system planning, including the future supply of gases (natural gas, biomethane and hydrogen) to dispatchable power stations and the switch of power generation facilities to hydrogen. Provide advice for gas network planning based on requirements of the whole energy system e.g. if certain dispatchable power stations are essential to electricity system operation and security of supply. Understand and assess the impact of the future of the gas networks on FSO’s gas functions and activities as suggested by Ofgem’s consultation on the role of the FSO ( i.e. gas strategic network planning, gas long-term supply and demand forecasting, gas market functions). | To be completed at later phase |  | 
H2
CCUS

## Slide 33
3.2 Use case 7
OFFSHORE WIND
1
Wind farm and electrolysis build
ELECTROLYSER
Constraint
ONSHORE WIND
2
Wind farm and CCGT conversion
Constraint
CCUS
3
Industrial cluster and blue hydrogen hub
4
Hydrogen storage to maximise recovery of renewable energy and provide seasonal storage
OFFSHORE WIND
NUCLEAR PLANT
5
Optimising a nuclear plant connection
HEAT
DHN
6
Future of gas network
H2 STORAGE
H2 CCGT
ELECTROLYSER
Convert from gas to hydrogen
INDUSTRIAL CLUSTER
BLUE H2 PLANT
NAT.GAS NETWORK
ELECTROLYSER
7
Flexibility of whole system options for long term planning and stability
ELECTROLYSER
POWER GENERATOR
H2 STORAGE
ELECTRICITY TRANSMISSION
CCGT
H2 NETWORK
Electricity network
Gas network
Hydrogen network
Carbon network
Heat network

## Slide 34
UC7: FLEXIBILITY OF WHOLE SYSTEM OPTIONS FOR LONG TERM PLANNING AND STABILITY |  |  | 
Goal | Ensure long term power network stability and resilience using efficient grid planning | Associated Synergies/ Benefits | Enable new revenue streams Facilitate innovation Increase efficiency of electricity system operation
“Networked Energy” Elements | Flexibility, storage, H2 production, onshore electricity and gas networks |  | 
Stakeholders | Storage owners, aggregators, DERs, ESO, DSOs, National Gas, SGU | Key Barriers and Dependencies | Modelling of various technologies Systems complexities and interactions Digitalisation is a key to improving efficiency in data exchange
Description | According to the ESO’s Future Energy Scenarios, operating a future energy system with high levels of renewables and no unabated natural gas generation will require significantly more flexible, zero carbon capacity. System stress will be driven as much by peaks and troughs in electricity supply and flows leading to the need for large amounts of short and diverse flexibility to accommodate different periods of high or low renewable generation and extreme weather events. The growth of distributed flexibility (flexible energy demand resources, such as storage, EVs, heat pumps and thermal storage, connected at distribution level) is a key enabler to achieving net zero with potential demand-side flexibility of 6-12 GW is predicted by 2040 from residential, commercial, and industrial sectors. In addition to the distributed flexibility, 50GW of offshore wind is expected by 2030. Interconnectors and long duration energy storage (LDES) is anticipated to reach a total 9 – 12GW in the South of England by 2030 and will be used to manage supply and demand and ensure security of supply in the 2030s. The new generation mix will be replacing traditional centralised generation (such as coal and natural gas) that typically provide resilience to the network. The FSO will need to conduct congestion and stability studies to understand the effect of all these new technologies on the system to support timely and coordinated process to maximise the network benefits and ensure that the transmission network can provide power to demand centres in a safe, reliable, and economic manner. Hence, the FSO should consider which option, or a combination of options, ensures long term power network stability and resilience by using efficient grid planning and operation while maintaining the grid stability. These options could be: 1- Distributed storage units, this could be individual storage units or virtual storage units (group of storage at different locations) providing congestion management and transmission and distribution deferral. 2- Demand side management especially when demand cannot be covered by green and cheap energy units rather than activating expensive and polluting production units or having to keep and maintaining expensive power plants for the winter peak. 3- Hybrid power plants (e.g. Wind + H2) providing energy services 4- Interconnectors and long duration energy storage (LDES) |  | 
What does it mean for the FSO? The role of FSO would be to: Consider all technology options during network planning across different vectors Understand impact of technologies on resilience, stability and on the net zero ambition Develop a business process by which the co-ordination, key dates, data exchange between the FSO and key stakeholders such (DSO, National Gas, SGU) is agreed Develop requirements to develop the digital twin of such technologies leveraging on the initial outcome of the Long Term Development Statement (LTDS), the GB CIM profile Set the rules for providing active distribution grids' dynamic response models to be delivered for dynamic stability studies, representing the dynamic behaviour in terms of voltage and frequency variations Define the network model and set of parameters to model the available technologies, as well as its combined response to frequency and voltage. Standardise network planning information exchange between different stakeholders Improve long-term plans methodologies to consider interaction between different sectors | To be completed at later phase |  | 
H2

## Slide 35: Section 4: Principles

## Slide 36: 4.1 Principles – Our Approach

## Slide 37
Table 4.1 - Type of whole energy system planning decisions
This section describes our approach to developing the principles of whole energy system optimisation for the FSO to apply in the network planning process. These principles could also set the basis for a multi-criteria decision-making (MCDA) analysis of whole energy system planning.
The role of principles was to guide the FSO during a decision-making process by explaining the optimisation problems the GB industry was facing and evaluating the proposed infrastructure options.
Before establishing the principles, it was important to understand the type of decisions the FSO would need to make or facilitate in the future.
Based on the use cases described in the previous section, we identified the following three broad types of considerations the FSO would need to advise on:
Trade-offs between electricity and gas (natural gas and/or hydrogen);
Optimal infrastructure delivery and efficient operation of the system; and
Strategic guidance for investors, infrastructure providers and market participants.
The table below shows the three different types of decisions that the FSO will need to advise on.
Decision type | Example
Needs Driven | Do we need an intervention/reinforcement?
Enabling Investment | What does the energy system need now to enable energy transition and support progress towards net zero in the future?
One or the Other | Should we choose among different vectors? Delivery times? Location? Technology? Scope? Cost?
The drivers behind each type of these decisions vary.
A “needs driven” decision typically reflects an infrastructure solution that is required to meet an assumed need, such as to connect new generation capacity, or to ensure security of supply and/or network resilience.
An “enabling investment” considers a potential benefit or synergy with a lesser degree of certainty, and seeks to anticipate (or even: encourage) market participants connecting generation/production capacity.
A “One or The Other” decision reflects an optimisation of different options or solutions (such as different vectors, delivery time, location, technologies) against a desired outcome.
4.1 Principles - Methodology

## Slide 38: 4.1 Principles - Methodology
Look into the objectives and the duties of the FSO
Define GLOBAL Principles that enable each objective
Identify the areas of FSO influence
Consider SPECIFIC trade-offs to inform decision making
Our methodology to develop the principles consists of 4 steps:
Step 1 – Look into the objectives and the duties of the FSO
We analysed the objectives and duties of the FSO and used them as guidance for the principles that the FSO needs to follow.
Step 2 – Define GLOBAL principles
We identified and defined the principles so that they enable the FSO to meet its objectives and its duties. We also used feedback from the workshop with ENA members to refine and enhance them.
Step 3 – Identify FSO areas of influence
We tested the principles in the use cases that we developed in phase 1 and identified a number of areas that the FSO could influence with regard to whole energy system planning.
For instance, the FSO can support investment decisions in specific network infrastructure. The FSO can also support decision-making regarding the timing, location, scope and technologies of network investments.
All these elements need to be taken into account when the principles are applied.
Step 4 – Consider SPECIFIC trade-offs
There are trade-offs and synergies that vary depending on the type of decision, the FSO areas of influence and the involved stakeholders. Although the ESO needs the principles to steer the direction of decision, at a later stage the FSO will also need to consider specific trade-offs that inform the decision making. These trade-offs include but are not limited to:
Effectiveness of the infrastructure solution to meet the FSO’s primary objectives.
Associated costs to inform whether the solution is economically optimal.
Feasibility of the solution including technology readiness and scalability.
Delivery risk, including supply chain considerations, permitting and consenting restrictions.
Stakeholder requirements to ensure that different perspectives and agendas are considered in the optimal solution.
Associated risk from wider reforms, such as connections reform or locational marginal pricing.
Fig 4.1 - Principles Methodology

## Slide 39: 4.2 Principles – Detailed Description

## Slide 40: 4.2 Application of principles
This section describes the principles that will provide the basis for FSO’s process for whole energy system planning.
In the first step, the principles enable FSO to meet its objectives.
In the second step of the process, the criteria enable FSO meet its duties.
The FSO must base its advice to government and Ofgem on a balanced assessment using all the principles in line with its objectives, giving due regard to the criteria given by its duties.
Application of the principles and criteria should be explored further in the next steps following this project. For example, the FSO could develop a process that ensures that the whole energy system solution achieves the fundamental principles or define binary conditions that solutions must have to meet the principles. The FSO could also decide to move these principles and criteria into a Multi-Criteria-Decision Making Analysis (MCDA) with weighted factors.
A detailed description of each principle is provided on slides 37 – 43.
Fig 4.2 – FSO principles of whole energy system planning
WESNP

## Slide 41: 4.2 Principles – Achieving net zero whilst maintaining security of supply
Principles | Description
Reduce carbon emissions | Description: The FSO must seek to enable network planning options and solutions that lead to a reduction in carbon emissions and enable the use of green energy (gas and power). FSO would need to agree the principles of emissions reduction calculations too so that it could be applied fairly to all connections. Use Case Example: In UC1, the development of the electrolyser will maximise the wind farm capacity (i.e. production of green electricity) and the generation of green electricity (i.e. due to the avoidance of curtailment) as well as production of green hydrogen. These outcomes all support a reduction in carbon emissions in the UK. Further considerations: Feedback from stakeholders suggested that lifecycle emissions could also be considered as well as the re-purposing of assets. Certainly FSO would consider directly related CO2, indirect carbon emissions should be further considered and align with the FSO sphere of influence. DNV highlights that international supply chain elements are out of scope.
Accelerate delivery of net zero | Description: The FSO must pursue options that should not only lead to lower carbon emissions but could also speed up decarbonisation and UK’s progress to net zero. Importantly, the FSO needs to consider the trade-offs of infrastructure development in light of boundary conditions set by timeframes, e.g., of increased speed of reduction in the shorter term, against security of supply in the longer term. Use Case Example: In UC3 each of the 3 options have an impact on the connection time of the windfarm. The FSO may need to take into account which of these options will be delivered sooner than the others whilst contributing to net zero. For example, the option to wait for the CCGT closure in 2035 could be the one with the greatest delay to the connection process and therefore slowest path to net zero. Further considerations: N/A
Table 4.2 – Detailed description of Achieving net zero principle

## Slide 42
Principles | Description
Optimise flexibility of gas and electricity systems | Description: To date, most system flexibility comes from turning up or down large coal and gas plants. This is no longer compatible with net zero targets, and hence low carbon alternatives have to be found, as set out in the government Smart Systems and Flexibility Plan (2021). The FSO must pursue infrastructure options that will increase the flexibility of the joint gas and electricity systems to respond to periods where additional supply is required to meet peak demand. Use Case Example: Depending on the type of flexibility required, from shaving peak demand to supplying power to the grid during low wind spells, different options will be more or less suitable and this principle should be considered in the context of a particular need. For example, UC 7 offers a number of short-term flexibility solutions, whereas UC4 explores hydrogen long-duration storage. Further considerations: As our networks and technologies, in general, become smarter, the FSO should in due course explore sources of flexibility from other sectors, such as heat (e.g. smart heat pumps).
Optimise whole system resilience | Description: Whole energy system planning should consider resilience for the energy system as a whole. Although electricity system resilience is well understood by the ESO, the FSO must seek to optimise (in technical and economic terms) resilience jointly across both the gas and electricity system. Use Case Example: UC6 indicates an example where whole system resilience should be considered and assessed during the transition of the gas networks, given interdependencies between gas network operation and power generation facilities that are currently run on gas. Further considerations : Stakeholders highlighted that as networks become more interconnected, co-ordination in gas and electricity systems operation is critical to manage the impact on resilience between vectors.
Table 4.3 – Detailed description of Security of Supply principle
4.2 Principles – Security of Supply [1/2]

## Slide 43
Table 4.4 – Detailed description of Security of Supply principle
4.2 Principles – Security of Supply [2/2]
Principles | Description
Optimise energy security and independence | Description: The FSO should consider how and at what scale different infrastructure solutions may facilitate GB’s energy security and, for example by relying mostly on domestic markets and regional energy solutions and less on imported energy. Use Case Example: Infrastructure solutions in use cases 1, 2, 4, and 5 all stimulate the production of clean domestic energy, therefore directly increasing energy security. The scale of energy security and independence that can be achieved varies across option under each of these use cases. Further considerations: In addition to facilitating UK energy independence, further considerations proposed by stakeholders involve the potential to expert energy (power, H2) to other markets.
Meet safety requirements | Description: Meeting safety requirements is a principle that must be met by all infrastructure options. Failure to meet safety standards would exclude infrastructure options from further assessment. Differences in safety risk, for instance from uncertainty around new technologies or in the delivery of infrastructure solutions must be factored into the FSOs assessment process. Use Case Example: Although not explicitly discussed in UC6, safety is a key requirement when transition gas to hydrogen networks. Further considerations: N/A
Table 4.3 – Detailed description of Security of Supply principle

## Slide 44
Principles | Description
Minimise costs to consumers | Description: Delivering energy transition requires unprecedented levels of investment, which are ultimately paid for by consumers. The FSO must pursue cost-efficiency delivery by maximising potential synergies and optimising trade-offs in gas and electricity infrastructure delivery, system operation and energy supply. Use Case Example: UC1 will have to consider the cost of reinforcing the electricity network, the cost of curtailing wind generation, and the cost of hydrogen network and storage infrastructure. Further considerations: This principle must be supported by a whole energy system cost-benefit analysis.
Deliver prompt and timely energy infrastructure | Description: The FSO must consider the timing of infrastructure delivery to ensure the new infrastructure is ready when it is needed and its value to consumers is maximised, without compromising security of supply, system resilience and net zero targets. Use Case Example: UC2 explores how to optimise synergies between a new wind farm connection and closure of an existing gas-fired CCGT plant without causing a capacity constraint. The FSO will have to consider the impact of delaying wind connection until 2035 on the whole energy system. Further considerations: N/A
Minimise disruption to consumers | Description: The FSO must seek to minimise adverse impacts on consumers from delivery/construction of network infrastructure. Infrastructure and engineering works can create disruption to consumers - subject to the location of the site - such as increase traffic of certain roads due to part closures, parking suspension for several hour or days, excess noise, waste and dust in the area around the site, short (un)planned outages of power supply, water supply or communication facilities. For example, the FSO should assess the delivery plan of investment options, the potential to avoid (repeated/unnecessary) engineering works, and maximise possible synergies from co-ordination of gas/electricity network construction activity, as well as with local authorities and possibly with other utilities. Use Case Example: UCs 1-6 involve new infrastructure construction, which will impact consumers during construction and operation. The FSO will have to acquire a detailed consumer impact assessment of each option from TOs and 3rd parties to understand the level of potential disruption and the scope for synergies. Further considerations: Close cooperation with local authorities could help the FSO and TOs and 3rd parties to gain better understanding on consumer impacts. This could include coordination with Local Authority Energy Plans (LAEPs).
Table 4.5 – Detailed description of Economic Efficiency and Coordination principle
4.2 Principles – Economic Efficiency and Coordination

## Slide 45: 4.2 Criteria - Facilitate Competition
Criteria | Description
Consider breadth of solutions | Description: The FSO’s options assessment process should ensure that all feasible and practical solutions have been taken into account, and that FSO recommendations do not impede or limit competitive delivery of infrastructure. This criterion does not propose that the FSO should favour one technology versus another, but seeks to ensure that no reasonable option overlooked. The FSO could also enquire whether market-based solutions have been considered. Use Case Example: UC5 considers multiple options for nuclear power use, from a traditional electricity supply directly to the grid, to thermo-chemical hydrogen production and suppling a District Heating scheme. Even though some technologies are less mature, it is still important to consider them. Further considerations: Stakeholders suggested to carefully consider the FSO’s role in developing new markets for other energy vectors, such as hydrogen.
Facilitate access to smaller market participants | Description: The GB energy market shows a growing number of smaller technologies and businesses, as well as more active consumers, or prosumers, that could provide valuable flexibility services to the grid, such as through V2G schemes or Demand Flexibility Services. As part of its assessment process, the FSO must reasonably avoid bias against smaller business and service providers, both in infrastructure delivery as well as in system operation. Use Case Example: UC7 considers different options to provide flexibility to the system, including (1) individual or virtual storage units, (2) demand side management and (3) a hybrid power plant. In its assessment, the FSO should be cognisant that option (3) would be less accessible for small market participants and factor this into its overall recommendation. Further considerations: Analyse how visibility of smaller providers of ancillary services can be improved in the Control Room
Table 4.6 – Detailed description of Facilitate Competition criteria

## Slide 46
Criteria | Description
Enable innovative solutions | Description: The FSO must not be biased in its assessment and consider, alongside traditional infrastructure options, new technologies, processes, commercial models and market-based solutions – as well as innovative hybrid solutions. At a minimum, the FSO must not, through its advice, unduly limit innovation in any of the above. Use Case Example: UC7 explores options for long-term power network stability and resilience and suggests a combination of solutions. These are 1) distributed storage units, 2) demand-side management, and 3) hybrid power plants providing energy services (e.g. wind and hydrogen). Further considerations: Linking to the previous criterion, enabling competition can support innovative solutions to unlock whole energy system benefits. Although out of scope for this project, the FSO could in due course explore innovative solutions through the interaction of the energy systems with connected systems, e.g. heat, agriculture, water and transport.
Table 4.7 – Detailed description of Facilitate Innovation criteria
4.2 Criteria - Facilitate Innovation

## Slide 47: 4.2 Criteria - Impact on Consumers
Criteria | Description
Accelerate connection processes | Description: Electricity networks are experiencing unprecedented requests for new connections to the grid, which in turn leads to delays in connecting customers. The FSO will need to take into account how network planning could alleviate this challenge and reduce connection time. Enhanced coordination between SO and TOs will help streamline the connections process, especially for renewable generation. This will not only help reach national green energy targets but will also make cheaper and cleaner energy available to consumers. Use Case Example: UCs 1 and 2 consider connection of wind power to the grid with known challenges, such as a connection behind a network constraint, timeliness of the connection, and maximisation of generation output. For example, UC2 has to specifically focus on options that avoid delaying connection of a wind farm, such as network reinforcement, earlier closure of the CCGT or creating local hydrogen demand. The option to wait for the CCGT to close down would delay the connection process, and the FSO would need to acknowledge this outcome and appraise it alongside other principles and criteria. Further considerations: n/a
Facilitate fair and inclusive transition | Description: In its appraisal of network infrastructure investments, the FSO must consider any potential adverse impact on customers and end-consumers from an economic, social, safety or security of supply perspective. Use case example: UC6 provides an example of running the electricity network during a partial switchover of the gas network to hydrogen. Important trade-offs should be considered during this process, such as the economic and system benefits from the switchover, and ensuring that no consumer is left worse off or at a safety or supply risk. Further considerations: Enhanced coordination with LAEPs and development of Regional System Planners will provide the next level of detail necessary to understand the full impact on vulnerable consumers.
Table 4.8 – Detailed description of Impact on consumers criteria

## Slide 48: 4.2 Criteria - Whole System Impacts
Criteria | Description
Enhance coordination across other networks | Description: Improved coordination across the systems is essential to deliver energy transition efficiently, this applies to both transmission-distribution coordination, as well as a wider cross-sector coordination. The FSO must take a holistic approach to network planning and consider what others are doing in this area, e.g. what regional solutions have already been considered to avoid duplication. Use case: In UC5, the FSO will have to advise on the best use of a newly connected nuclear plant. Among other factors, the FSO will have to consider the impact on other networks and how this might affect their development plans. For example, they will have to consider whole system impacts from a nuclear plant supplying power to a particular District Heating scheme. Further recommendations: Explore possible cross network databases
Enable Whole-System Ready Solutions | Description: The energy transition is an inherently complex and multifaceted processes and cannot be approached by considering individual energy vectors and industry sectors in isolation. For example, the interdependency between electricity, gas/hydrogen, transport, water and industrial sectors is expected to increase in the future. Whilst not clearly in its Day 1 remit, the FSO would need to consider solution that are capable in the long run of accommodating or even optimising outcomes across these sectors. Use case: All use cases presented in this project are capable of considering whole-system solutions, but for this project, focus on networked energy. Further recommendations: See recommendations in section 5
Consider Environmental Impact | Description: Above and beyond carbon emissions, the FSO must consider wider environmental impacts, such as, among others, air quality, biodiversity impacts, waste, water usage, and impacts on areas of natural beauty. Use case: All use cases enable consideration of environmental impacts from network planning options. Further recommendations: Stakeholder feedback proposes a detailed assessment of any use case should perform a full Environmental Impact Assessment (EIA), which would include a Habitant Regulations Assessment (HRA).
Table 4.9 – Detailed description of Whole System Impacts criteria

## Slide 49: 4.3 Principles – Illustrative Application

## Slide 50: Applying the principles to Use Case 1
To provide a more tangible example of how the FSO could apply the principles to inform its assessment and recommendations , we have elaborated Use Case 1 which looks into maximising the wind capacity built and the energy recovery from that capacity under specific constraints.
The principles will steer the analysis and decision-making process to inform the FSO’s recommendation for the optimal infrastructure solution by considering the comparative benefits and risks of different approaches and solutions. For example, in Use Case 1 the FSO will need to compare which option achieves a greater overall carbon emissions reduction, but it will also assess which option advances GB to net zero faster.
It is worth highlighting that our application of principles in this example is illustrative and does not provide any recommendations at this stage, as a more detailed assessment approach (built upon the necessary tools) would be required to come to a recommendation. In real-life examples, the results can be expected to vary significantly, depending on the specifics of each network planning challenge. In other words: the “right” answer will differ between use cases, even where the assessment covers the same parameters.
The worked example on the next page aims to highlight the complex nature of the assessment the FSO will need to carry out. This assessment covers multiple interdependent and dynamic factors, whose outcomes cannot always be fully foreseen or objectively confirmed, but require case by case interpretation and assessment.
Problem statement | What is the optimal strategy for connecting a new offshore wind farm behind a constrained area of the electricity transmission network to avoid curtailment of the wind farm?
Options | 1) Reinforce the electricity network; 2) Strategically place an electrolyser that will produce green hydrogen during periods of high wind and low electricity demand.

## Slide 51: Applying the principles to Use Case 1
Principles | Option 1 : Reinforce electricity network | Option 2: Electrolyser installation | Notes
Reduce carbon emissions | This option would reduce carbon emissions through an increased level of generation of renewable energy from the wind farm, displacing thermal (fossil fuel) generation. | The use of the electrolyser will maximise the wind farm’s capacity (i.e. production of green electricity) and the generation of green electricity (i.e. due to the avoidance of curtailment) as well as production of green hydrogen. | Relevant carbon emissions must be calculated using a fair and consistent approach that includes the appropriate counterfactual for each option.
Accelerate delivery of net zero | Comparative assessment of the timeline to deliver network reinforcement or the electrolyser plus any supporting infrastructure. Option 2 might fit better with government net zero targets and (hydrogen) policy, and could be more versatile – and therefore possibly faster - in enabling multiple routes to decarbonisation. | Option 2 may align better with net zero targets and UK’s policy around hydrogen development. Delivery timeframe to be confirmed, expected to be longer than option 1 due to the need to develop an electrolysis plant. | The FSO will need to consider the timeline of the delivery but also how each option aligns with net zero targets.
Optimise flexibility of gas and electricity systems | Although reinforcement of the electricity network may relax some transmission constraints, it does not typically add much flexibility in terms of managing demand and supply. | The electrolyser can provide additional flexibility because it can use wind power when demand for electricity is low and produce hydrogen which can be used to meet other types of demand requirements (subject to transport and storage). | The FSO will seek to understand how each option increases the flexibility of both gas and electricity system and explore whether whole system synergies can be achieved by the different options.
Optimise whole system resilience | Traditional reinforcement options would primarily enhance resilience for the electricity system. | Whole system resilience is demonstrably supported by the production of green hydrogen alongside renewable power. | The FSO would need to consider both direct and indirect resilience impacts.
Optimise energy security and independence | Both the production of domestic offshore renewable electricity and green hydrogen increase GB energy security and independence. Option 2 could be more versatile as it enables both power and hydrogen, but it would need to be established whether its net contribution is greater than option 1. | The production of domestic offshore renewable energy and green hydrogen increases energy security and independence of GB as it adds to the energy mix. | The FSO must compare how much the two options contribute directly and indirectly toward energy security and independence.
Meet safety requirements | To be considered a viable solution, either option would need to meet minimum safety requirements. | Both options should meet the safety requirements. | Minimum safety requirements must always be met, but the FSO could assess whether either option provides wider/enhanced safety outcomes.
Minimise costs to consumers | Cost include the capital and operating cost for network reinforcement, the curtailment costs of wind generation under existing and potential future market conditions. | Cost include the capital and operating cost for the electrolyser, hydrogen network and possibly hydrogen storage. | The FSO will need to minimise the cost to consumers. At this stage we have considered delivery costs and constraint management costs.
Deliver prompt and timely energy infrastructure | Comparative assessment of the timeline to deliver network reinforcement or the electrolyser plus any supporting infrastructure. The FSO will need to consider if delivery timeline aligns with licence requirements, customer expectations and economically optimal delivery. |  | The FSO must consider the timing of infrastructure delivery to ensure the new infrastructure is ready when it is needed and its economic benefits maximised.
Minimise disruption to consumers | Comparative assessment of the potential disruptions from engineering works. Other considerations involve challenges with planning applications/ permitting and local stakeholder impacts. |  | A detailed delivery plan would be required for the FSO to properly assess this principle for each solution.

## Slide 52: Section 5: Gap analysis and recommendations

## Slide 53: Gap Analysis & Recommendations
Following our analysis and stakeholder feedback, we identified gaps in evidence and provided recommendations for further research, analysis and potential projects to build on the knowledge of whole energy system coordination.
This section highlights key gaps, and offers recommendations for FSO to close these gaps, across the following areas:
  Technologies
  Skills, knowledge and resources
  Coordination with other vectors
  Business processes
  In addition, engagement with industry stakeholders throughout this Project has highlighted gaps in awareness of policy and governance around the FSO role. Continual engagement with the industry will provide additional clarity on the expectations of the new organisation.
  We discuss the key gaps, and advise that the ESO should continue to table these topics for discussion with DESNZ, Ofgem, gas and electricity networks, and wider energy sector stakeholders. The ESO’s objective should be to obtain clarity on relevant permanent arrangements, where possible, before the FSO goes live (expected in 2024) – or at least to ensure that, where the arrangements remain unclear, the impact on its role is commonly understood.

## Slide 54: Technology Gaps
To keep to a manageable number of use cases, this project has not covered all technologies that could be considered within whole energy system co-ordination. Some of these technologies already have a meaningful role in the GB energy system, some are used to a limited extent, some are technologically feasible but have not yet been deployed at scale in GB, and some lie further down the technology and commercial readiness scale.
Technology
Recommendations
The FSO will need to be aware of the potential development / deployment of technologies to provide an evolving view of their impact on network planning and how they should be further considered in whole energy system planning processes. For example, the FSO will need to take regard of:
  The timelines and scales that technologies could be deployed;
  What their impact on emissions could be;
  What their risks / benefits and trade-offs are;
  How much they will cost and the impact on consumer bills;
  How they might influence markets and end user behaviour;
  How they will impact the operation of the electricity and gas systems.
The FSO will need to identify an ongoing process by which it monitors the deployment of such technologies to respond appropriately to their introduction and incorporate them and their potential impacts into future plans. For example, the FSO could use the Future Energy Scenarios process as a basis for regular stakeholder engagement, knowledge gathering and analysis.
Current or potentially available technologies:
  Hydrogen import/export
  Hydro and tidal power
  Pumped storage
  Geothermal power
  Desalination with excess/constrained power
  Power to X (methanol, SAF etc.) for bulk liquid export of constrained power
  Large scale biomass for BECCS
  Hydrogen to natural gas via methanation with captured (bio or grey) CO2
Technologies which are less mature:
  Small modular nuclear reactors
  Hydrogen gas engines and turbines
  Direct air capture with excess/constrained power
  Reversible fuel cells i.e. natural gas/hydrogen to power or power to hydrogen
  Large scale electrical storage – flow batteries
  Seasonal thermal energy storage
  Floating solar
  Fusion (very long term)

## Slide 55: Skills, Knowledge and Resources - Gaps
Our gap analysis has focused on the high-level skills, resources and knowledge that the FSO will need to further develop to enable an efficient and more coordinated whole energy system planning process across different energy vectors. Acknowledging that the FSO comes from an electricity-focused knowledge base, we have identified the following:
The use cases have shown the FSO will need to co-ordinate and engage with multiple stakeholders at a greater level than current ESO teams are doing. As such we see that the FSO will need to develop skills, knowledge and processes to co-ordinate more effectively across all energy vectors, and understand stakeholders’ strategies, objectives and targets and their impact on the FSO strategy and objectives. Two-way communication will be key to greater engagement and building trust between stakeholders, so the FSO will need to continue to communicate their strategy and aspirations to audiences that come from different backgrounds.
The FSO will also need to consider and communicate how a GB whole energy system planning process and model is developed. In section 4.2. we have made a few recommendations on next steps following the development of the principles. When looking into detailed network planning process and model, we acknowledge that the FSO will require the skills, resources and knowledge to effectively coordinate the analysis that is required.
More specifically, looking into the principles that we have developed, the FSO will require resources to perform the assessment of whole energy system principles, and develop them further into a methodology which enables decision-making and options assessment.
Recommendations
In order to address gap 1, the FSO could first consider the development of a whole energy system coordination plan. The project would help the FSO understand detailed resource requirements and skills, the need (or not) to create a team and make multi-vector engagement plans with both technical roles and decision makers. The FSO could start testing co-ordination ideas with key stakeholders and build a trusted environment across all sectors and organisations.
In order to address gaps 2 and 3, the FSO will need first to design a whole energy system planning process which will provide the FSO and GB plc with an approach to options assessment for whole energy system.
The high-level approach will identify synergies and collaboration opportunities which can be achieved between vectors, data exchange and communication requirements. We do not envisage at this stage a detailed planning model, but a methodology which building upon existing knowledge and process across all organisation, not only the FSO.
Coordinated recommendations will need clear and transparent decision analysis techniques. An essential output will be communicating the coordinated recommendations across different energy vector stakeholders and government. As a first step, the FSO should consider the resources and skills and establishment of new teams and roles, that are required to design this approach and based on the outputs of the project, the FSO will further consider how to operate this methodology/ model.

## Slide 56: Co-ordination Gaps
Gaps in co-ordinated activities across vectors to facilitate whole energy network planning and decision making include but are not limited to the following:
Gas and electricity networks work in silos, bringing their own perspectives, strategies and objectives. Less effective communication affects not only network planning activities, but general knowledge and skills sharing. In addition, energy networks could benefit from the wider communication of the different perspectives, advantages, disadvantages and trade-offs of network planning options across all energy vectors.
Variable levels of engagement between networks and local authorities. Although this is an area which energy networks and local authorities are seeking to improve, there is still a lot to be done especially in relation to greater alignment between Local Area Energy Plans (LAEPs) with networks’ forward plans. Local authorities will require support from network companies as they may not have the skills and/or the capacity to perform these activities .
In one of the use cases, we have identified the need to co-ordinate during the transition of current gas network to low carbon fuel networks (e.g. hydrogen networks, biomethane networks) or the development of new hydrogen networks. Although this is a gap that highly depends on policy decisions surrounding hydrogen for heat, the gap in understanding the role of electricity networks during this transition and the impact of the transition on the electricity networks should be further explored.
Co-ordination
Recommendations
There are several projects and initiatives that could fill in the gaps in co-ordination across different vectors and sectors. We have identified tangible future steps that the FSO could undertake alongside other networks:
Secondments between gas and electricity networks would help workforce expand their skills and knowledge to other vectors. Secondments could take place not only within GB but also in collaboration with European networks, especially where there is an opportunity to share best practices.
Key stakeholders across the energy sector (e.g. networks, academia, consultancies) could work together to build a knowledge base for wider stakeholder dissemination. For example, to collate a set of briefing notes that capture the differences in operating and planning electricity and gas networks. In this way, the networks could deliver a tangible output for the industry and also promote engagement, knowledge sharing and building trust. The FSO could co-ordinate or even initiate this initiative.
The energy sector would benefit from the development of a holistic network design process that included different energy vectors, i.e., an expansion of the one that was developed by the ESO for offshore and onshore networks planning – the Holistic Network Design (HND).

## Slide 57: Co-ordination Gaps
Access to standardised high-quality data, that are more accessible to a wider set of stakeholders. Particular examples are the current lack of a national building stock model; a register of all low-carbon technologies; a register of energy network assets. These would enable alignment of inputs that feed into network planning models of networks, and Local Area Energy Plans.
This project has not developed any use cases that require the co-ordination of the energy sector with the water, transport or waste sectors. As discussed, the scope of the project focused on the co-ordination requirements between gas, electricity, hydrogen and CCS.
In addition the project has not focused on the development of markets that facilitate whole energy system solutions. Network planning and market development remain largely independent of each other across the industry. A standardised holistic approach could help unlock further benefits by considering both 'hard' (network reinforcement) and 'soft' (market) solutions to various challenges.
Co-ordination
Recommendations
The FSO will need clarity on their potential role around Regional System Planning (RSP). Once this is established, the FSO will need to consider what type of collaboration and alignment is required with local authorities. Due to the status of the RSP consultation decision, we do not recommend any further steps at this stage.
Future innovation projects could explore the interaction, dependencies and opportunities for collaboration and co-optimisation between the energy sector with water, transport and waste sectors.

## Slide 58: Tools, ICT, Data Gaps and Business Processes
Our analysis showed the optimisation problems the FSO will encounter in the future will become increasingly more complex and interdependent on different technologies and changing patterns of supply and demand. Advanced analytical tools, as well as a review and update of business processes, will be required.
All use cases presented in this project considered at least two different energy vectors, such as offshore wind and electrolysis for hydrogen development. As some of these situations are not yet operational, there are a lack of automated data flows between involved parties and wider stakeholders. This ultimately results in siloed organisations and manual data sharing.
Current methodologies do not consider new technologies and the new role of the FSO. There is also a lack of a comprehensive suite of whole energy system tools, that will allow a holistic appraisal of multiple technologies.
As the volume of data that the FSO will have to process on a daily basis for various activities continues to grow, reliance on tools such as Microsoft Excel, will become a significant blocker to efficient operation, and in some cases could even limit the analytical capacity which is critical to many internal and external processes.
Transparency around processes, analytical methods, modelling and data are key to building trust across different stakeholder groups.
Recommendations
Develop a whole energy system data co-ordination and management strategy. This could include, but is not limited to, the following activities:
  Evaluate data standards and work with others to improve these
  Establish data that the FSO needs for its planning and operational roles and develop common data structures for 3rd parties to share these data
  Formulate requirements for data exchange
  Utilise artificial intelligence and machine learning techniques to add value to data
Review existing methodologies and business processes, such as long-term planning (CSNP), to decide if any updates or new processes are needed to create a balanced representation of electricity and gas needs. Consider what cross-system interactions are missing and fill in the gaps.
Building on the whole energy system cost-benefit analysis, assess the landscape of tools and approaches that could be used for cross-vector option evaluation, assessment of guiding principles and multi-criteria decision analysis. This may require development of a suite of new tools. In the section around skills and resources, we have already highlighted the need to expand skills and resources and potentially build a team to perform impact assessment of whole energy system options. The plan to update skills and resources should align with the assessment and potential development of a suite of new tools.

## Slide 59: Policy Gaps
Governance Gaps
The future of hydrogen, how and where it is produced, stored, transported and used, is fundamental to the role of the FSO. Pertinent to the FSO’s understanding on network infrastructure requirements with sufficient certainty will be decisions on:
    Hydrogen blending in the transmission system;
    Hydrogen usage for heating and I&C sector;
    Hydrogen storage for system resilience and security of supply;
    Hydrogen production from small nuclear reactors;
  In addition, ESO is working with Ofgem and government to further clarify responsibilities for (whole energy) system operation.
  System operation outcomes (for instance: constraint payments to wind generators) have been a key part of Ofgem’s assessment of transmission network investments under RIIO. The FSO would have the capability to plan network investments to optimise its future need/deployment of electricity balancing services. In a whole systems environment, however, this would need to include optimising gas (hydrogen) balancing outcomes.
  From a policy perspective, assuming gas system operation will continue to sit with NGT, there will need to be a clear basis for collaboration and coordination, data gathering and exchange, and decision-making (including primacy between molecules and electrons – for instance in the context of supply and demand shocks).
The FSO role is positioned as an advisory role to government and Ofgem to ensure whole system impacts can inform policy and regulatory decision-making.
the ESO is working with Ofgem and government to understand how FSO advice will be used consistently to inform regulatory (funding) decisions by Ofgem to ensure licensee and project-specific assessments align with whole systems planning considerations.
In terms of government (DESNZ) policy decisions, the relationships with (policies developed by) local authorities and devolved governments should also be prioritised as lack of clarity, and may give rise to primacy considerations and potential conflicts that would impede whole systems planning.
At various points in the future, there will be methane, pure hydrogen, and blended networks in development/operation. The conversion of the gas networks from natural gas to hydrogen or hydrogen blends therefore requires coordination at national level to ensure safety and consistency of solutions/technologies deployed and full alignment across the supply chain. The governance process of this transition and clarity on FSO’s role herein are significant developments that will facilitate this coordination.
The government’s current position is that it will provide the FSO with statutory powers to request data/information from other licensees. Roles and responsibilities for data security, quality and consistency and indeed the treatment of commercially sensitive information should be further defined. We note that whole systems planning would be informed by data from non-licensed industry participants. Further clarity on the governance around the scope and use of data – including potentially the establishment of a dedicated independent body for the sharing of energy data (data warehouse function) – should be considered.

## Slide 60: Section 6: Next Steps

## Slide 61: Next Steps
Project WESNP has showcased the complexity of the whole energy system network planning task for the FSO, which requires an understanding of both existing and potential future interactions between gas (natural gas and/or hydrogen) and electricity network infrastructure delivery and operations. With this understanding, the FSO must identify interdependencies, trade-offs and synergies to make recommendations as to the best outcome for “GB plc”. The challenge is that the “best” outcome is determined through interpretation of multiple interdependent and dynamic factors. Project WESNP has also provided a principles approach for whole energy system optimisation for the FSO to apply in the network planning process and provided recommendations on
As a priority the next steps for the ESO are to:
Seek further coordination with National Gas Transmission (NGT) to establish the basis for future collaboration, systems and data sharing, and skills development;
Continue close coordination with Ofgem and DESNZ to drive/support policy decisions that will ensure effective implementation and operation of the FSO;
Continue engaging closely with other stakeholders (e.g. TOs; DNOs; GDNs) to establish the basis for future collaboration as well as systems and data sharing, including alignment with previous work on the Centralised Strategic Network Planning (CSNP) process;
Develop new (and/or improve) data building, gathering and exchange processes and protocols, as well as develop IT-based solutions to be in place in time to support the FSO role;
Develop detailed whole energy system planning processes to enable the unbiased and effective options assessment and network planning process; and
Develop the tools and processes needed for its options assessment process.

## Slide 62: Appendix

## Slide 63: List of abbreviations
BECCS | Bioenergy with carbon capture and storage | FSO | Future system operator
CC(U)S | Carbon capture (usage and) storage | H2 | Hydrogen
CCGT | Combined cycle gas turbine | HND | Holistic Network Design
CSNP | Centralised strategic network planning | HRA | Habitant Regulations Assessment
DER | Distributed energy resources | LAEP | Local Authority Energy Plans
DESNZ | Department for energy security and net zero | MCDA | Multi-Criteria-Decision Making Analysis
DHN | District heat network | NGT | National Gas Transmission
DNO | Distribution network operator | NTS | National transmission system
DSO | Distribution system operator | OCGT | Open cycle gas turbine
Dx | Distribution | SGU | Solar generation unit
EIA | Environmental impact assessment | TO | Transmission owner
ENA | Energy network association | Tx | Transmission
ESO | Electricity system operator | V2G | Vehicle to grid

## Slide 64
About DNV
DNV is the independent expert in risk management and assurance, operating in more than 100 countries. Through its broad experience and deep expertise DNV advances safety and sustainable performance, sets industry benchmarks, and inspires and invents solutions. Whether assessing a new ship design, optimizing the performance of a wind farm, analyzing sensor data from a gas pipeline or certifying a food company’s supply chain, DNV enables its customers and their stakeholders to make critical decisions with confidence. Driven by its purpose, to safeguard life, property, and the environment, DNV helps tackle the challenges and global transformations facing its customers and the world today and is a trusted voice for many of the world’s most successful and forward-thinking companies.