## Slide 1: SPEN Predict4Resilience
Show and Tell Webinar
23 May 2022

## Slide 2: Context, Opportunity, Solution, Strategic Alignment
Predict4Resilience – Weather Fault System
Context
A resilience approach to understanding uncertainties helps critical infrastructure to continue to provide the essential services on which society depends. In 2020, the National Infrastructure Commission (NIC) recommended a framework for resilience which anticipates future shocks and stresses; improves actions to resist, absorb and recover from them by testing for vulnerabilities; values resilience properly; and drives adaptation before it is too late.
Opportunity
Currently, predicting and decision-making regarding faults comes from tacit knowledge of experienced personnel. This presents an opportunity to transform operational practices through the use of a data driven approach to fault prediction. This would make it possible to predict weather events more accurately with longer visibility and identify its impact in order to protect supply.
Solution
The aim is to use advances in supercomputing and numerical weather prediction to combine state-of-the-art weather forecasting and novel statistical post-processing to better predict short-term adverse weather impacts and resultant faults on the network.
This Weather Fault System (WFS) will assist engineers to make more informed decisions based on actionable fault and risk predictions, leading to better preparedness against adverse weather events and increased operational efficiency.
Strategic Alignment
The WFS is strongly aligned with NIC recommendations, i.e., enabling Control Room Engineers to better anticipate shocks to the network, to develop more informed response plans for swift and efficient recovery, to log decision-making processes and evidence thus facilitating lessons learnt to adapt and transform systems.
Notes: Storm Arwen, November 2021
Extreme wind speeds and cold temperatures caused loss of power to 1M+ households, and 100K+ were without power for several days. 13 of the 14 network licence areas were impacted, with the most severe damage to SSE Power Distribution, SPEN, Northern Powergrid and Electricity Northwest networks.
Storm Eunice, February 2022
Strong winds brought down trees on power lines causing 1M+ households to lose power, with succeeding storms’ Dudley and Franklin resulting in ongoing power cuts lasting several days. These impacts were felt right across the UK electricity network.

## Slide 3: Project Background
SIF Collaboration Partners
A consortium of collaborators including University of Glasgow, Met Office, and Arup is formed under the Predict4Resilience (P4R) project, which is led by ScottishPower Energy Networks (SPEN), for the Discovery Phase.
P4R Collaboration
ScottishPower
Energy Networks
University of Glasgow
Met Office
Regulated Distribution Network Operator leading the SIF collaboration.
Arup
In Discovery, University of Glasgow is leading a preliminary proof of concept for the fault forecast and a survey data requirements and availability.
Subject-matter Expert supporting on weather and weather forecast data, and weather forecast methodologies.
In Discovery, Arup is providing engineering support on fault data analysis and processing, as well as leading the production of a high-level functional specification and a high-level business case.

## Slide 4: Weather Fault System
Functional Specification – Technical Components
User Interface (UI)
The UI will expose application functionality to end users. The UI may be a commercial-off-the-shelf application (such as ESRI Geographic Information System (GIS)) or a bespoke application (such as SPEN’s Predictive Analytics of Energy (PRAE) application) which could be further developed to realise the required functionality.
Fault Forecasting Engine (FFE)
The FFE is the core processing element of the WFS utilising statistical analysis techniques to predict network faults given weather forecast data. A knowledge base shall be maintained to track the accuracy of the WFS which can be used to develop and train Control Room Engineers. Reporting and alerting functionality will provide automated alerts when fault predictions exceed agreed thresholds.
Data Store
The data store shall provide a centrally available store of weather and fault data for the WFS – capable of elastic scaling to support growth of the WFS across national and international DNOs.
Figure 1. Building blocks and technical components of the WFS
Technical Components
Notes: A suitability assessment of UI options will be undertaken during the Alpha phase, including evaluation of options capable of integrating with other DNO systems to provide additional data to assist with response planning.
Relevant datasets are expected to include: weather forecast data, network fault data, satellite imagery and Lidar data (as required by the forecast model development).

## Slide 5: Weather Fault System
Functional Specification – End Users, User Stories, Requirement Catalogue
Control Room Engineers
Control Room Engineers use information to enhance how perform their day-to-day, make decisions, and allocate resources. These users generally work to a short-term horizon which means they want to plan for one to three days out.
Data Scientist
This user will need to access historical performance data and system logs in order to improve the application and modelling.
Control Room Trainee
This user may need specific scenario based training to better learn how to use the application and/or shadow a primary user with existing knowledge.
System Administrator
This user will need to set up new instances of the application for new clients/ control rooms and assign users
User Stories
Based on user research with primary users, we have organised requirements into high level “epics”, including:
Current Conditions
Predicting Conditions
Ongoing Learning
Administration
Requirement Catalogue
An initial requirements catalogue has been developed for the Weather Fault.
1. General | 2. Technical | 3. Functional | 4. NonFunctional
Requirements that define business policies, standards and needs. | Requirements that state the technical policies and constraints. May refer to technical infrastructure. | Requirements that set out the features that the application should provide. | Requirements that define how well the application will operate.
1.1. Branding | 2.1. Hardware | 3.1. Data Entry | 4.1. Archiving & Retention
1.2. Business Constraints | 2.2. Interoperability | 3.2. Data Maintenance | 4.2. Availability
1.3. Business Policies | 2.3. Software | 3.3. Presentational | 4.3. Back-Up / Recovery
1.4. Cultural |  | 3.4. Procedural | 4.4. Capacity
1.5. Language |  | 3.5. Retrieval | 4.5. Performance
1.6. Legal |  |  | 4.6. Security
 |  |  | 4.7. Usability

## Slide 6: Weather Fault System
Business Case – Benefits and Costs
Efficiency benefits
The WFS can transform human-centric decision-making practices. Integration of weather conditions into asset health information will enable improvements in asset management and allow better asset protection. Further, users can log and store decisions made on forecasts to support lessons learnt and knowledge sharing. The WFS also supports embedding data-related skills in SPEN.
Quantitative benefit
Consultation with SPEN’s Control Room Engineers flagged savings in the CML cost of network faults caused by “Wind and Gale (excluding Windborne Material)” as the core benefit in Discovery. This benefit is achieved by better response planning and resource mobilisation in advance, based on the forecasted location and number of faults.
Assumptions on CML cost savings
The CML cost of a “do nothing” scenario (the counterfactual) is estimated based on historical fault data for the 10-year period from 2011 to 2020, excluding those faults covered by exceptional events where penalties do not apply. The
baseline for annual savings is assumed to be 5%.
Development cost
SPEN currently has a bespoke software application i.e., the PRAE application, which is considered to be of similar scale of functional and infrastructure requirement in comparison to the WFS. Hence, the initial outlay for the WFS is assumed to be in a similar order as the PRAE’s development cost of approximately £1m.
Operational cost
The following three key elements form the minimum requirement for the operational cost:
Notes: Other opportunities for savings
Depending on the type of faults, the WFS may help avoid interruptions to customers and bring CI cost savings by enabling proactive repairs and network management based on the forecasted location of network faults.
Better resource mobilisation and maintenance planning enabled by the WFS, may reduce abortive costs (e.g., cancelling planned works) which would generate savings.
Other considerations
CML cost savings will increase substantially when other weather-related faults are considered, such as those caused by “Snow, Sleet and Blizzard”. These savings will be captured as the WFS forecast model is developed further in Alpha phase.
DNO-dependent costs
The operational costs associated with weather data supply, server hosting and other IT infrastructure may increase based on the number of DNOs using the WFS, the amount of data supplied and the capacity required to host it. It is assumed that these two operational costs will multiply in accordance with the number of DNOs using the WFS.
DNO-independent cost
Unlike the operational costs related to the supply of data and infrastructure, it is assumed that the support and development costs, in essence, can be shared amongst the application users. Hence, this operational cost will remain the same regardless of the number of DNOs using the WFS.

## Slide 7: Weather Fault System
Business Case – CBA
Methodology
The quantitative analysis is based on the baseline investment required for the WFS (i.e., the initial outlay of £1m for the application development) and the net savings (i.e., the savings in the CML cost less operating and maintenance costs of the WFS), in order to calculate:
The benefits / costs ratio;
The Net Present Value (NPV); and
The payback period.
Assumptions on rollout
It is assumed that SPEN will be the initial user of the WFS, and starting from Year 2 of the WFS being live, other DNOs will begin to use the WFS, i.e., rolling out the WFS to the rest 5 DNOs at a pace of 2 new DNOs each year.
Assumptions on timeline
The cost savings (i.e., the benefits) will continue to be generated as long as the WFS is operational. Nonetheless, in order to calculate the “benefits / costs ratio” and “NPV”, the timeline for the estimate is assumed to be 10 years, and a discount rate of 3.5% is applied where needed, to be in lined with the HM Treasury Green Book discount rate.
Baseline financial metrics
Using a 10-year assessment period, the benefit/cost ratio is 1.76x.
Using a 10-year assessment period and 3.5% discount rate, the NPV is c.£430k.
With the baseline assumptions, the payback period is 6 years in order to recover the initial investment, as seen below.
Notes: DNO-dependent costs
The operational costs associated with weather data supply, server hosting and other IT infrastructure may increase based on the number of DNOs using the WFS, the amount of data supplied and the capacity required to host it. It is assumed that these two operational costs will multiply in accordance with the number of DNOs using the WFS.
DNO-independent cost
Unlike the operational costs related to the supply of data and infrastructure, it is assumed that the support and development costs, in essence, can be shared amongst the application users. Hence, this operational cost will remain the same regardless of the number of DNOs using the WFS.

## Slide 8: Met Office
Review of existing ensemble numerical weather prediction products

## Slide 9: Review of existing ensemble numerical weather prediction products
Megan Pearce
Scientific Consultant
Dr Joe Osborne
Industry Consultancy Manager

## Slide 10: Ensemble prediction systems
An ensemble forecast is generated by running a forecast model multiple times from slightly different starting conditions
  this can be used to help quantify sources of uncertainty
A number of candidates with strong performance over the UK domain have been identified
Different EPS provide forecasts over different:
  time horizons
  spatial resolutions
It may be appropriate to consider the use of multiple EPS, either individually or as a multi-model configuration
Notes: Different EPS provide forecasts over different time horizons and spatial resolutions, and therefore it may be appropriate to consider the use of multiple EPS, either individually or as a multi-model configuration, to achieve useful forecasts over the full time horizon of interest that utilise the highest resolution models

## Slide 11: Verification and application
This covered sources of ‘truth’
The choice of verification method depends on:
  forecast type (deterministic vs probabilistic)
  specificity (for example, yes/no, categorical or continuous).
Ensemble forecasts require post-processing because they contain errors in both statistical location and in dispersion
  various systems (Met Office IMPROVER)
  machine learning techniques
Multiple examples of EPS in operational decision making away from energy sector
Hagelin et al (2017)
Hagelin, S., Son, J., Swinbank, R., McCabe, A., Roberts, N. and Tennant, W., 2017. The Met Office convective-scale ensemble, MOGREPS-UK. Quarterly Journal of the Royal Meteorological Society 143, pp2846-2861. https://doi.org/10.1002/qj.3135
Notes: There are a number of sources of ‘truth’ that can be used for forecast verification, including raw observations at synoptic weather stations, gridded observational datasets and modelled truth such as reanalysis and hindcast datasets.
The work then talks about a number of methods to verify forecast performance, specifically ensemble performance. These include brier score, ranked probability score, continuous ranked probably score, ROC curves and reliability diagrams.
ensemble forecasts require post-processing because they contain errors in both statistical location (ensemble members are away from the actual state of the atmosphere but relatively near each other) and in dispersion (the ensemble can under or over represent forecast uncertainty).
The are Multiple examples of EPS in operational decision making away from energy sector. An example of a Hazard Impact Model to support decision-making is the Vehicle OverTurning (VOT) model. An example of using a multi-model ensemble in flood forecasting.
The Advanced Weather Forecasts for Dynamic Line Rating delivered by the Met Office in collaboration with National Grid Electricity Transmission (NGET) looked to explore the use of NWP models as input to an overhead line (OHL) rating forecasting model, in order to generate ensemble forecasts of overhead line ratings that could be implemented in an operational dynamic line rating (DLR) system. https://www.nationalgrid.com/national-grid-partner-met-office-boost-capacity-electricity-transmission-network . The project explored a number of potential post processing techniques for the use in forecast system validation and optimisation. For example, a dependency on topography was shown during the forecast validation, and therefore the opportunity to use LIDAR techniques to derive terrain height and improve wind forecast in sheltered areas was identified. Machine learning methods such as quantile regression forest and neural networks were considered as a theoretically plausible replacement of the physical model for calculating the rating of a section of overhead line, identifying the potential in the future to generate rating forecasts directly from NWP models, although this is not currently operationally implemented. The additional use of machine learning techniques such as generalised linear models to learn and correct for model biases, could also improve the NWP forecast input feeding the machine learning rating forecast model.

## Slide 12: Recommendations
The recommendations for exploration in Alpha phase are as follows:
Two separate ensemble prediction systems, run in parallel, with differing time horizon focus. In this set up, it is suggested that an ensemble over the short lead time (up to 5 days) would be utilised in a risk threshold approach for operational decision making, whilst a second ensemble would be utilised within a weather pattern approach for awareness of the developing broader scale conditions on a medium range time horizon (up to 15 days)
MOGREPS-UK / UKV (Met Office)
ENS / HRES (ECMWF)
Blend models from two centres to create one seamless, probabilistic forecast over full time horizon. This forecast could then be utilised for either risk-based threshold decision-making or weather pattern analysis.
MOGREPS-UK / ENS (Met Office/ECMWF) – Utilise techniques in literature, such as Beck et al. (2016) and Met Office IMPROVER, to blend models from different forecasting centres. The aim would be to produce one consistent, seamless forecast from 0-15 days, with relative weighting to models as appropriate.
Verification of forecast accuracy could be undertaken using:
  the Midas-open (temperature and wind), HadUK-Grid (precipitation) datasets and ERA5 (wind, taking advantage of the complete spatial coverage but recognising the limitations that exists with reanalysis wind fields).
Notes: The use of a high resolution 18-member ensemble generating hourly forecasts using time-lagging techniques. In literature, the current configuration of MOGREPS-UK was shown to perform better out to 5 days when compared to UKV, but pairing MOGREPS-UK with UKV is also recommended.
It is anticipated that the verification of forecast accuracy (forecast of meteorological variables rather than the faults themselves) could be undertaken using the Midas-open (temperature and wind), HadUK-Grid (precipitation) datasets and ERA5 (wind, taking advantage of the complete spatial coverage but recognising the limitations that exists with reanalysis wind fields). The importance of observations and the error associated with them should not be overlooked and testing against more than one dataset for historical forecast verification is recommended.
The Alpha phase should look to implement standard measures for verification as noted from the literature (such as Wilks, 2011a; Porson et al., 2020), both in terms of forecast accuracy and ensemble performance, with a particular consideration towards the use of neighbourhood approaches over point verification (section 2.2). Additionally, the literature has highlighted a number of post-processing techniques that can be utilised to improve both forecast skill and ensemble performance such as batch-processing using EMOS, Kalman filtering and machine learning. Given the active research in post-processing of ensemble forecasts, there is interesting scope to explore the implementation of adaptive and real-time processing methods that use the ensemble forecast spread to further improve upon the forecast skill and ensemble performance – a distinct advantage of ensemble over deterministic forecasting. However, the extent to which more involved techniques, such as machine learning, could be explored in Alpha will depend on the availability of suitable training data over the region of interest and may be beyond the timescales and scope of this project phase.

## Slide 13: Review of existing capability
Existing capability:
Modest academic/industry literature
Very few related products
Analysis:
Predicting specific faults from weather is extremely challenging
Predicting number of faults in a region is possible
No fault forecasting capability presently exists that meets DNO’s requirements
Learnings to be taken from the literature
Existing research focused on weather-fault relationship and/or short-term or storm forecasting only
Wilkinson et al (2022) “Consequence Forecasting: A Rational Framework for Predicting the Consequences of Approaching Storms,” doi: 10.1016/j.crm.2022.100412
Cerrai et al (2019) “Predicting Storm Outages Through New Representations of Weather and Vegetation.” doi: ACCESS.2019.2902558.

## Slide 14: Sample Dataset and Exploratory Analysis
ERA5 Reanalysis (estimates of actual weather)
  2010-2021
  Regular gird over GB
  Resolution (1h/31km)
Ensemble Numerical Weather Predictions - ECMWF
  2018-2021
  50 ensemble members
  Resolution (3h/55km)
Merged with wind-fault data prepared by ARUP
Above: Wind-related faults per day by wind speed, direction (ERA5, district mean), and time of year. Only days with three or more faults are included.
Below: Example 14-day ensemble weather forecast for the Borders issued on 10/01/2018 (50 members, black) and the ERA5 “truth” (red).

## Slide 15: Initial fault forecasting
Historic weather and fault data
Weather-fault model
Weather forecast
Fault forecast
Explanatory “features” engineered from weather data
Statistical model based on extreme value theory learned from data
Daily faults predicted by district from 1 to 14 days ahead
Proof-of-concept: scope for improvement!!!

## Slide 16: Forecast performance
Summary
Performance similar from 1 to 5 days ahead
  Dominant source of uncertainty: weather-fault relationship
Performance degrades from 5 to 14 days ahead
  Weather forecast uncertainty grows
  Still some skill at 14 day

## Slide 17: Looking ahead
Forecasting engine
Improve specificity and accuracy:
  Higher weather resolution data
  New data (weather variable, vegetation, topography)
  Other fault types
  Algorithm development
Testing and validation
Tool design and development
Engagement with potential user groups
UX and UI design and development
Prototype of backend
Commercialisation
User engagement: multiple DNOs
Benefits assessment
Go to market strategy

## Slide 18: Appendices

## Slide 19: Appendix 1 – NIC Resilience Framework

## Slide 20: NIC Resilience Framework

## Slide 21: Appendix 2 – User Stories

## Slide 22: User Stories
Based on user research with primary users, we have organized requirements into high level “epics” (or scenario level) and “user stories” (task level). The epics include Current Conditions, Predicting Conditions, , Ongoing Learning, and Administration.
# | As a Control Room Engineer I want to… | So that I can…
 | View a list/map of network faults that are predicted to occur within a district due to the latest weather forecast . | Understand potential resource needs
 | View a list/map providing information how network faults vary over time due to the latest weather forecast . | Understand potential resource needs
 | Sort/select by region for more details on network faults in that region | Understand region specific need
 | Understand the range of potential network faults that may occur within a region – including the probability of occurrence | Consider the likely impact of a weather event
 | View a summary of the weather forecast | Better predict fault impact
 | View a summary of the dominating weather event | Better allocate resources
 | Sort/select by Region for more details on local weather conditions (i.e wind speed, type of weather, weight of snow, temperature) | Understand details as they impact the plan
 | View planned work/ ongoing customer effecting work | Understand workload to inform the incident response plan
 | View planned customer effecting work thresholds (max, med, min numbers) | Understand workload
 | View a list/map of all active response teams | Understand workload
 | View a list/map of all planned response teams | Understand workload
 | Sort/select by region for more details on response teams assigned to faults | Understand workload
 | Edit/save details on work teams assigned to faults | Adjust staff allocation
 | View new assets in regions (what % of assets have been changed) - to provide some context for why faults may have increased or decreased | Understand asset history
 | Log / Save my assessment/actions due to the forecasted network faults. (i.e. Category event, probability score, response team plan) | Capture my decision
 | Log / Vote on if the tool impacted my decision / actions | Capture my decision
 | Share insights or planning tools with colleagues (i.e. response managers, district managers) | Better inform others to may need to act
Epic 1: Current Conditions

## Slide 23: User Stories
Epic 2: Predicting Conditions
# | As a Control Room Engineer I want to… | So that I can…
 | Adjust time (i.e. day to storm) and type of weather to model potential faults | Model different scenarios
 | Edit/ Tag a fault by Category Event | Alert colleagues to potential faults
 | View a list of response plans based on category event | Better inform my plan
 | Select a specific category event response plans | Better inform my plan
 | View a category event response plan that provides common response scenerios based on my weather category event, time of week context, etc. | Better inform my plan
 | View if seasonal checks in a region have been completed | rule out errors
 | Alert a Sr Manager if Five Days out and potential severe weather | Inform others with key tasks
 | Alert a District Manager if Three Days out and potential severe weather | Inform others with key tasks
 | Log / Save my assessment/actions due to an active weather fault. (i.e. Category event, probability score, response team plan) | Learn post event
 | Log / Vote on if the tool impacted my decision / actions | Learn post event

## Slide 24: User Stories
Epic 3: On-Going Learning
# | As a Control Room Engineer I want to… | So that I can…
 | View a list of past event events by region, type, date, and/or engineer. | Select a past event
 | Select event to review actual results (i.e. response team plan) | See specific results
 | View assessment/actions due to an active weather fault. (i.e. Category event, probability score, response team plan) | See specific results/ learn to inform future predictions
 | Log / Vote on actual vs predicted | learn to inform future predictions
# | As a Data Scientist I want to… | So that I can…
 | Review historical data and usage | Understand trends
 | Calibrate prediction models | Improve accuracy
 | Integrate new data sets or algorithms | Enhance the application

## Slide 25: User Stories
Epic 4: Administration
# | As a System Administrator I want to… | So that I can…
 | Set up a new instance of the Weather Fault application | Customize for new clients
 | Add relevant branding / logos | Customize for new clients
 | Assign user and permissions | Customize for new clients

## Slide 26: Appendix 3 – CBA Sensitivity Studies

## Slide 27: CBA Sensitivity Studies
The graphs below show the payback period and NPV sensitivities on the benefits, Capex and Opex.
As seen in the graph, the project is less sensitive on both Capex and Opex, but relatively sensitive to the benefit of the WFS, i.e., the cost savings. A 1% improvement in the benefits could reduce the payback period by 1 year. It also increases the NPV by c.£503k and 1% reduction in benefits also reduces the NPV by c.£503k.
On capex, a movement of +/-10% has a limited impact on the payback period. In order to have 1 year reduction in the payback period, the initial capex will have to be reduced by c.30%. Regarding impact on NPV, +/-10% on Capex translates to c.+/-£97k.
On opex, it has a limited impact on the payback period. On NPV, a +/-10% in opex translates to +/-c.£112k.
These sensitivity results show that the successful cost savings delivered by the WFS is paramount to the success of the project.

## Slide 28: Appendix 4 – Delivery Plan

## Slide 29: Delivery Plan